________

COMX-35

Superboard   V1.2 (FW Build 200 – PC SW build 91)

Manual

© Copyright Ed Keefe & Marcel van Tongeren, 2013-2016

# Table of contents

Table of contents	2

COMX USB Interface – PC Software	6

Installation and set-up	6

About	6

USB Settings	6

Online Settings	7

Delete back-up	7

PC Disk  Access	8

[STR=] USB PLOAD,”filename” [,start] [,S] [,R] [,start,B] [,Bx]	8

USB PSAVE,”filename” [,start] [,start,end [,B] [,D]] [start,end,exec] [,Bx]	8

[STR=] USB DLOAD,”filename”	9

USB DSAVE,”filename”	9

[STR=] USB BLOAD,”filename” [,Bx]	9

USB BSAVE,”filename” [,Bx]	9

[STR=] USB DEL,”filename” [,A] [,B] [,I] [,R] [,T] [,X]	10

INT = USB COMP(”filename1”,”filename2” [,B] [,I] [,R] [,T])	10

[STR=] USB CD [,”dirname”]	10

USB MKDIR,”dirname”	10

USB RMDIR,”dirname”	11

USB CAT [/W]	11

RAM Bank Access	12

USB RLOAD (bank)	12

USB RSAVE (bank)	13

USB MOVE (start, end, destination [,force [destination slot, destination bank]])	13

Clock	14

USB CLOCK (x)	14

USB RTCFT (x)	14

USB RTCPC	14

STR = USB DATE	14

USB DATE,”xx/yy/zz”	14

STR = USB TIME	14

USB TIME,”hh:mm:ss”	15

USB TIMEAM,”hh:mm:ss”	15

USB TIMEPM,”hh:mm:ss”	15

COMX Configuration	16

USB LINE	16

USB SCREEN	16

USB SCREEN (x)	16

USB COLOR (x)	16

USB CTONE (x)	17

USB CHAR [(x)]	17

USB FLASH (x)	17

USB LOGOTUNE (x)	17

USB BOOTMSG (x)	18

USB GO40	18

USB GO80 [(x)]	18

VOLUME (x)	18

USB SYSDISP	18

USB SYSDEF	18

NVRAM	20

USB NVLOAD	20

USB NVSAVE	20

USB SYSLOAD	20

USB SYSSAVE	20

USB NVLIST	20

USB NVPOKE (nvram address,value)	21

[STR =] USB NVPUT (id, source, number of bytes)	21

[STR =] USB NVGET (id, destination)	22

[STR =] USB NVPUT (id, value <INT>, string <STR>)	22

STR  = USB NVSGET (id)	23

INT = USB NVIGET (id)	23

USB NVSTART (start)	23

USB NVCLR	23

USB NVDEL (id)	24

I/O	25

INT = USB JOY (1) / INT = USB JOY (2)	25

INT = USB INP (port)	25

USB OUT (port, value)	25

USB Q (value)	25

INT = USB Q	25

INT = USB EF (x)	25

Internet Access	26

USB ONLINE (x)	26

[STR=] USB URL,”url”	26

[STR=] USB URL (link number)	26

[STR=] USB URLGET (screen)	26

USB URLDISP	26

USB BROWSER [,”url”]	27

USB EMAIL	30

[STR=] USB HSWEB	30

Turbo Tape	32

USB TLOAD[+]	32

USB TSAVE[+]	32

USB TDLOAD[+]	32

USB TDSAVE[+]	32

Printer	33

USB PON	33

USB POFF	33

USB PTV (x)	33

USB PCNTL (x)	33

USB PKB (x)	33

USB PMEMDUMP (start, end)	33

USB PTEST	34

USB PSET	34

USB PLIST	34

USB PPR / USB PPRINT	34

F&M Monitor	35

USB MON	35

USB DMON	35

Games	36

USB TENNIS	36

USB SPACE	36

USB WORM	36

COMX DOS to PC	37

USB IMGTEST,”filename”	37

USB IMGTODISK,”filename” [/DR]	37

USB DISKTOIMG,”filename” [/DR]	37

Graphics	38

USB GRAPH	38

USB GRAPH (graphic screen)	38

USB PLOT (x, y, color)	40

USB PLOT (x, y, color, character)	40

USB LINE (x, y, color, x2, y2)	40

USB CIRCLE (x, y, color, radius)	40

USB ELLIPSE (x, y, color, a, b)	40

USB DCHAR (state)	41

USB SHAPE (character, shape string)	41

USB TV (state)	41

USB PPOKE (page RAM address ,value)	42

USB CPOKE (address, value) / USB CPOKE (character, line, value)	42

INT = USB CPEEK (address) / INT = USB CPEEK (character, line)	42

USB DWIDTH (state)	43

USB DHEIGHT (state)	43

REM adaptation	44

USB LIGHTRM line	44

USB HIDERM line	44

RENUMBER extension	45

RENUMBER start, end [,line] / RENUMBER [line]	45

Slot And Card Access	46

CARD B (x) or CARD Bx	46

[INT =] CARD B	46

CARD S (x) or CARD Sx	46

INT = CARD S	46

[INT =] CARD F (x) or [INT =] CARD Fx	46

USB	47

COMX DOS	48

DOS BOOT	48

DOS INIT	48

DOS STARTUP	48

DOS LABEL,”diskname” [/DR]	49

DOS DATE,”date” [/DR]	49

DOS LOCK [,”filename”] [,D] [,W] [/DR]	49

DOS UNLOCK [,”filename”] [,D] [,W] [/DR]	49

DOS DISKCOPY	49

DOS FILECOPY	49

Other Commands	50

USB VER	50

USB OLD [,defus address]	50

USB HELP [,“command”]	50

USB HISTORY	50

STR = USB HEX (value)	50

STR = USB BIN (value)	50

INT = USB POS (row, column)	50

USB MEMDUMP (start, end)	51

Screen Editor	52

Other features	52

Bug fixes	53

Extra Features	53

APPENDIX A – MEMORY MAP	54

COMX & Super Board Memory MAP	54

Super Board EPROM Content	54

APPENDIX B – DETAILED MEMORY MAP	55

BASIC ROM (0000 - 3FFF)	55

RAM (4000 - BFFF)	61

SB ROM Bank 0 (C000 - DFFF)	63

SB ROM Bank 1 (C000 - DFFF)	65

SB ROM Bank 2 (C000 - DFFF)	66

SB ROM Bank 3 (C000 - DFFF)	67

SB ROM Bank 4 (C000 - DFFF)	68

SB ROM Bank 5 (C000 - DFFF)	69

SB ROM Bank 6 (C000 - DFFF)	70

SB ROM Bank 7 (C000 - DFFF)	72

SB RAM Bank 8-12 (C000 - DFFF)	75

SB RAM Bank 13 & 14 (C000 - DFFF)	75

SB RAM Bank 15 (C000 - DFFF)	75

SB FW ROM (E000 - E7FF)	76

EXPANSION ROM (E800 - EFFF)	78

NVRAM & RTC (F000 - F3FF)	80

Character Memory (F400 - F7FF)	82

SB FW ROM / Page Memory (F800 - FFFF)	82

APPENDIX C – PC <-> COMX HEADERS	86

Standard Header (COMX <-> PC)	86

CD Header (PC -> COMX)	88

URL,”url” Header (COMX -> PC)	88

URL (x) and URLLINK (x) Header (COMX -> PC)	88

CAT Header (PC -> COMX)	89

Image file Header (COMX <-> PC)	90

APPENDIX D – ERROR MESSAGES	91

COMX 35 BASIC Error Messages	91

F&M BASIC V2.00 Error Messages	93

PRINTER Error Messages	93

COMX 35 DOS Error Messages	94

SB Error Messages	95

APPENDIX E – BASIC COMMAND TABLE	97

# COMX USB Interface – PC Software

## Installation and set-up

Before installation of the USB SW first connect the SB to the COMX and the SB via a USB cable to the PC. This should install the device driver software. If windows cannot find the drivers automatically they can be downloaded from: http://www.ftdichip.com/FTDrivers.htm (download VCP Drivers?).

After installation of the USB SW start it via the start menu (note that the next time your PC is started the USB SW will start automatically), this will add an icon in the taskbar that looks like:

This means the USB SW is running but no connection is found to the COMX as yet.

To get the connection working first identify the serial port used by the driver SW. To do this: start the Control Panel, select Hardware and Sound and then the Device Manager. Search for the entry Ports (COM & LPT) and take note of the port number indicated as ‘USB Serial Port’, this value is needed to be filled in the settings dialog.

To open the settings window, go to the icon in the taskbar and select ‘Setting…’ with the right mouse button. Now fill in the port number as ‘COM Port’ and make sure the ‘Speed’ is set to the same value as is selected by the jumper on the SB board (default 57600).

Press ‘Save’

The taskbar icon should now change to:

Note that the icon will change back to the yellow warning sign as soon as the COMX is switched off. When the COMX is switched back on it should switch back to the green icon within a few seconds.

If in some cases the green icon does not appear, the following could help: open the Device Manager via the control panel and select ‘Scan for hardware changes’.

## About

To open the about window: go to the icon in the taskbar and select ‘About…’ with the right mouse button. This will show the COMX USB Interface version and build number as well as the FW build number (if available), copyright message, link to COMX SB web site, special thanks and license information.

## USB Settings

To open the settings window: go to the icon in the taskbar and select ‘USB settings…’ with the right mouse button. Note that when settings are saved by pressing the ‘Save’ button the USB interface is restarted and the current directory on the COMX will also be reset to the ‘Root’ directory.

Other settings:

Root – Either use the ‘Root’ button or change the path manually to change the root directory seen from the COMX. The selected root is the highest directory level that can be accessed by the COMX. This is either shown as directory \ or \top-directory on the COMX (depending on ‘Show to directory in USB CD’ setting)

COM Port – Specify the COM Port as used by the ‘USB Serial Port’ found in the Device Manager.

Speed – 57600 or 115200 baud. When changed make sure the jumper on the SB board is changed accordingly

Show top directory in USB CD – Select Yes / No, ‘No’ will show the root directory as \, ‘Yes’ will show the root directory as \top-directory (i.e. \Comx when the default root folder is used).

Case conversion – These settings are only used if USB CHAR(0), normal COMX character set or USB CHAR(1), lower case ‘default’ standard COMX characters on ‘SHIFT’ are selected. USB CHAR(0) is set as default. For these character sets the USB SW will convert any filename or directory name as specified: in lower case, upper case or capitalized. Default all filenames will be in lower case and directory names capitalized. When USB CHAR(2) or (3) are used the capitalization is as typed on the COMX.

Back-up – Select Yes / No, ‘Yes’ will result in creation of a back-up file for the specified commands with the format ‘nameNumber.type.bak’. So when saving a file ‘happiehap.comx’ the first back-up file created will be named happiehap1.comx.bak, second happiehap2.comx.bak etc. ‘No’ will result in a question on the COMX to overwrite the file Y/N when the file already exist on the PC.

Save – Save current settings

## Online Settings

To open the online settings window: go to the icon in the taskbar and select ‘Online settings…’ with the right mouse button.

Define the Player name and location as used in the USB HSWEB command. Note that the maximum length of both player name and location is 25 characters and the following characters are not allowed and will be ignored: # ~ ; :.

To be able to get your email address specified as sender with USB EMAIL make sure to fill in a correct and valid email in the ‘Email address’ field

Home page and bookmark fields are used by the USB BROWSER command and can be shown on the COMX by pressing the ‘H’ or 0 to 9 keys during a browser session. Max length of these fields is 126 characters. To store a bookmark press the ‘Store’ button.

Email address and aliases are used by the USB EMAIL command. Any defined alias can be edited when selected by the Aliases choice button. A new alias can be stored when ‘alias / email address’ is shown. To store the alias press the ‘Store’ button.

## Delete back-up

To open the delete back-up window: go to the icon in the taskbar and select ‘Delete back-up…’ with the right mouse button. This will open the Delete back-up window, showing all back-up (.bak) files in the specified root directory and sub directories. Pressing ‘Yes’ will delete all these files ‘No’ will just close the window.

# PC Disk  Access

## [STR=] USB PLOAD,”filename” [,start] [,S] [,R] [,start,B] [,Bx]

Load any program .comx file into COMX RAM memory. When optional parameter ‘R’ is used the loaded program will automatically be started with a RUN or CALL command.

Default BASIC .comx file content will be loaded starting at address @4400. If however a ‘start’ value is used the content will be loaded starting at the specified address (rounded to lower 256 bytes). So ‘start’ value @4560 will result in a load to @4500. The ‘start’ value can be any 16 bit hexadecimal or decimal value as well as a variable expression. Note however that a variable expression starting with ‘R’, ‘S’ and ‘B’ is not allowed.

Machine code .comx files (saved with ‘start’ and ‘end’ address) will always be loaded at the same address used during the save command.

To load a binary (.bin) file specify optional parameter B and the start address.

Optional parameter ‘Bx’ will execute a BLOAD command loading the specified .ram file to bank x or all banks (BA) after the .comx or .bin file is loaded. So using parameter ‘Bx’ will result in loading of two files first the .comx or .bin file and then the .ram file, both with the same filename. If the first file is not found the loading will be stopped and a ‘file not found’ error will be shown. If the second file is not found the first file will already have been loaded and a ‘RAM bank file not found’ will be shown.

Optional parameter S will show:

- The start, end and exec addresses if a pure assembler (ASM) file is loaded

- The start and end addresses if a binary (BIN) file is loaded

- The start address if an assembler & BASIC (A&B) file is loaded

- ‘Basic only’ if a BASIC (BAS) file is loaded

USB PLOAD can also be used to load directly to the SB RAM banks or a COMX 32K RAM card. To do so select the desired RAM bank (CARD Bx) and the use a USB PLOAD command. The program to be loaded needs to be able to RUN in @C000-@DFFF range. Also the program should have been saved from @C000 or loaded with a start address of @C000.

NOTE: USB PLOAD with option R will not work when loading directly to a RAM card as the SB FW will be switched in before execution of the RUN or CALL command.

If optional parameter STR is specified the return string will contain the possible error code: ‘File not found in directory’ or ‘RAM bank file not found’ if the specified file or RAM bank file (option Bx) is not found. In this case any running program will not ‘break’ and the user program can handle the error code. If the file is found an empty string will be returned.

## USB PSAVE,”filename” [,start] [,start,end [,B] [,D]] [start,end,exec] [,Bx]

This will save the current program to a .comx file. Any BASIC program will be saved as well as any assembler code before DEFUS address. When F&M BASIC 2.0 is loaded this command will only save BASIC (from address @6700).

When only optional parameter ‘start’ is specified the current program in memory is only saved from specified address. This can be used for saving only the BASIC part of a program by using the DEFUS value as start address.

When optional parameters ‘start’ and ‘end’ are used the specified part of COMX memory between ‘start’ and ‘end’ address will be saved to a .comx file. Optionally ‘exec’ can be specified as well for the execution address. The execution address will be used when a USB PLOAD with parameter ‘R’ is given to start the machine code program at the correct address.

Parameter ‘B’ can be used to save the specified part of COMX memory from ‘start’ to ‘end’ address to a .bin file.

Optional parameter ‘Bx’ will execute a BSAVE command saving content of bank x or all banks (BA) to the specified .ram file after the .comx or .bin file is saved. So using parameter ‘Bx’ will result in saving of two files first a .comx or .bin file then the .ram file, both with the same filename.

Parameter ‘D’ can be used to save (or dump) the specified part of COMX memory from ‘start’ to ‘end’ address to a .txt file.

Start, end and exec values can be any 16 bit hexadecimal or decimal value as well as a variable expression. Note however that a variable expression starting with ‘B’ and ‘D’ is not allowed.

USB PSAVE can also be used to save directly from any selected expansion card. To do so select the desired cards (CARD Sx) and the use a USB PSAVE command with a range of @C000-@DFFF.

## [STR=] USB DLOAD,”filename”

Load data area for string and arrays from a .comx file.

If optional parameter STR is specified the return string will contain the possible error code: ‘File not found in directory’ if the specified file name is not found. In this case any running program will not ‘break’ and the user program can handle the error code. If the file is found an empty string will be returned.

## USB DSAVE,”filename”

Save data area for string and arrays to a .comx file.

## [STR=] USB BLOAD,”filename” [,Bx]

Load data from indicated .ram file directly to (RAM) bank x, where x can  be 8 to 15. In this case max 8KB is loaded from the .ram file.

If x=A is used (or Bx is omitted) all RAM banks will be loaded (max 8*8K = 64K).

If optional parameter STR is specified the return string will contain the possible error code: ‘RAM bank file not found’ if the specified file is not found. In this case any running program will not ‘break’ and the user program can handle the error code. If the file is found an empty string will be returned.

## USB BSAVE,”filename” [,Bx]

Save data to indicated .ram file directly from (RAM) bank x, where x can  be 8 to 15. In this case 8KB is saved to the .ram file.

If x=A is used (or Bx is omitted) all RAM banks will be saved (resulting in a 8*8K = 64K file).

## [STR=] USB DEL,”filename” [,A] [,B] [,I] [,R] [,T] [,X]

Delete ‘filename’.

If no additional parameter is given the file with filename.comx will be deleted. If other file types need to be deleted the following parameters can be used:

- All 5 defined file types: Emma 02 (.comx), binary (.bin), image (.img), RAM bank (.ram) and text (.txt) files

- Binary files (.bin)

- Image files (.img)

- RAM bank files (.ram)

- Text files (.txt)

- Delete all back-up files with extension .comx or with extension as indicated with A, B, I, R or T parameters.

If optional parameter STR is specified the return string will contain possible error code: ’Could not delete file’ if the specified file name is not found or an error caused the file not to be deleted. In this case any running program will not ‘break’ and the user program can handle the error code. If the file is found an empty string will be returned.

## INT = USB COMP(”filename1”,”filename2” [,B] [,I] [,R] [,T])

Compare filename1 with filename 2, if the files are identical 0 is returned if not the location of the first difference is returned.

If no additional parameter is given files with filename1.comx and filename2.comx will be compared. If other file types need to be compared one of the following parameters can be used:

B: Binary files (.bin)

I: Image files (.img)

R: RAM bank files (.ram)

T: Text files (.txt)

## [STR=] USB CD [,”dirname”]

Change to sub directory ‘dirname’, also return the path from the PC (if the path is >127 characters, just the last 127 are printed). If no directory name is specified the PC path is returned without any change. Directory name “..” will go up one directory level. Note that only one directory name can be given per USB CD command.

Examples:

A$=USB CD

-> Assign current path to A$

USB CD,”Games”

-> Change directory to directory ‘Games’ if it is available

PR USB CD,”Games”

-> Change directory to directory ‘Games’ if it is available and print full path

## USB MKDIR,”dirname”

Create sub directory ‘dirname’

## USB RMDIR,”dirname”

Remove sub directory ‘dirname’

## USB CAT [/W]

Show current directory content (or catalog to use COMX terminology). USB CAT will use the COMX DOS format. USB CAT/W will show a condensed format with 2 filenames per line and all directories marked with ‘*’

# RAM Bank Access

## USB RLOAD (bank)

Load program stored in (RAM) bank 8 to 14 to main RAM. Program to be loaded will be stored in main RAM location 4400h to 63F8h.

USB RLOAD/RSAVE/OLD can be used to design a program using > 32K as follows:

- Main RAM area 4400h - 63FFh (8K) to be used as ‘swap’ area.

- Main RAM area 6400h – end main RAM (~B6xx) to be used for the main program. This is about 20K.

- Bank 8 to 14 to be used to swap to 4400h – 63FFh area, this is 7*8K which is 56K. In theory allowing a 56K + 20K = 76K program.

Example:

Write the following program in main RAM:

DEFUS @4400

10 PRINT “BANK 8”

20 USB OLD,@6400

30 GOTO 40: REM Continue main program on line 40

USB RSAVE(8)

DEFUS @4400

10 PRINT “BANK 9”

20 USB OLD,@6400

30 GOTO 10: REM Continue main program on line 10

USB RSAVE(9)

DEFUS @6400

10 PRINT “MAIN”

20 USB RLOAD(8)

30 GOTO 10: REM Start program swapped in from bank 8 on line 10

40 PRINT “MAIN”

50 USB RLOAD(9)

60 GOTO 10: REM Start program swapped in from bank 9 on line 10

This stores 2 small programs in bank 8 and 9. The 3rd and main program starting at 6400h will load the program from bank 8 and start it at line 10, then a jump will be made back to the main program at line 40 which will load the program from bank 9 etc.

Note 1: after an USB RLOAD the program loaded at 4400h area HAS TO be continued, the main program can only continue after a USB OLD,@6400.

Note 2: Before any string or array variable is set the main program needs to have been started. Any sting or array variable that is assigned in the program in the swap area BEFORE the main program has executed will be erased when the main program starts execution. This will NOT be the case after first execution as long as the program is not ‘ended’ or stopped with ‘ESC’.

## USB RSAVE (bank)

Save current program in main RAM to RAM bank 8 to 14. Program to be saved can be max 8K large and should be stored in main RAM location 4400h to 63F8h.

See USB RLOAD for an example of how USB RLOAD/RSAVE can be used to design a program using more than 32K.

## USB MOVE (start, end, destination [,force [destination slot, destination bank]])

Move / copy memory part from start to end to the requested destination. Source and destination can overlap.

If optional force parameter is omitted or 0 a warning will be given on any move command with a destination overlap to ROM or unsafe RAM areas (4000-43FFh, BF00-BFFFh and stack area). With force parameter <> 0 the move command will be executed without any warning.

Source location (if between C000h-DFFFh) is always from the current selected slot and bank (as selected via CARD Bx), destination  slot and bank can optionally be specified in the command. Note a copy to C000h-DFFFh will always give a warning unless force = 1 is specified.

# Clock

## USB CLOCK (x)

x=0: Remove and stop the clock at top right of screen

x=1: Show clock at top right of screen, when program is running (after a RUN, CALL, USR or USB PLOAD,”filename”,R, DOS RUN) the clock will not be shown.

x=2: Always show clock at top right of screen even when a program is running (some SW might turn the clock of if the SW has their own interrupt routine).

x=3: Same as 0

## USB RTCFT (x)

Set RTC FT to x (0 or 1), for details see M48T58 data sheet.

Any other uneven value of x will have the same result as 1, even same as 0.

## USB RTCPC

Fetch PC date and time and set RTC accordingly. This command will also fetch the date and time (24H or 12H) format from the PC and store it into NVRAM for use with USB DATE and USB TIME commands.

## STR = USB DATE

Read the current date and return it to specified string variable or print it. Resulting string is formatted according to the PC format as received by USB RTCPC.

## USB DATE,”xx/yy/zz”

Set date according to specified string value, string value should be formatted according to the PC date format as received in USB RTCPC. Note that the separator is also fetched from the PC and could for example be a ‘/’ or ‘-‘. A PR USB DATE will show the current separator format.

Note that an error code will be given if an incorrect date is specified. The command will check on format, invalid month (>12) and invalid day (depending on month and/or leap year).

## STR = USB TIME

Read the current time and return it to specified string variable or print it. Resulting string is formatted according to the PC format as received by USB RTCPC, i.e. if the PC is using a 24 hour format the TIME command will do the same, if the PC uses a 12 hour format the TIME command with do the same and add AM or PM to the end of the string.

## USB TIME,”hh:mm:ss”

## USB TIMEAM,”hh:mm:ss”

## USB TIMEPM,”hh:mm:ss”

Set time according to specified string value. Use TIMEAM to set the time in AM format, TIMEPM for PM format. All 3 commands will work independently of set clock type.

# COMX Configuration

## USB LINE

Deactivate F&M Screen Editor and activate COMX Line Editor

## USB SCREEN

Activate F&M Screen Editor and clear screen

## USB SCREEN (x)

Set COMX BASIC current and startup background screen color, where x is defined as:

1: Black

2: Green

3: Blue

4: Cyan

5: Red

6: Yellow

7: Magenta

8: White

Original COMX BASIC command SCREEN(x) still changes the current background color as before. However the value is not saved in NVRAM, so after a restart or power off/on the background color as defined with USB SCREEN (x) will be used as start-up color. Default startup color is black.

## USB COLOR (x)

Set COMX BASIC current and startup character color, where x is defined as:

|  | Normal text / <comxcharlow> | URL links / <comxcharhigh> |
| --- | --- | --- |
| 1 | Black | Green |
| 2 | Red | Yellow |
| 3 | Blue | Cyan |
| 4 | Magenta | White |
| 5 | Black | Blue |
| 6 | Red | Magenta |
| 7 | Green | Cyan |
| 8 | Yellow | White |
| 9 | Black | Red |
| 10 | Blue | Magenta |
| 11 | Green | Yellow |
| 12 | Cyan | White |

Original COMX BASIC command COLOR(x) still changes the current character color as before. However the value is not saved in NVRAM, so after a restart or power off/on the character color as defined with USB COLOR (x) will be used as start-up color. Default startup color is 12, cyan/white.

## USB CTONE (x)

Set COMX BASIC current and startup character color mode, where x is defined as:

0: Normal color mode

1: Black and white mode

Original COMX BASIC command CTONE(x) still changes the current character color mode as before. However the value is not saved in NVRAM, so after a restart or power off/on the character color mode as defined with USB CTONE (x) will be used as start-up color mode. Default startup color mode is 0.

## USB CHAR [(x)]

x = 0 to 3: save 'x' in NVRAM

x = 4 to 7: do NOT save 'x' in NVRAM

Shape character set:

x = 0 or 4: Standard COMX characters (upper case ‘default’)

x = 1 or 5: Lower case ‘default’ standard COMX characters on ‘SHIFT’

x = 2 or 6: Upper case ‘default’ and lower case characters on ‘SHIFT’

x = 3 or 7: Lower case ‘default’ and upper case characters on ‘SHIFT’

For value 0 to 3 the selected character set will be re-shaped at the next COMX boot if NVRAM is available.

When no (x) is specified USB CHAR will re-shape the last selected character set.

Every USB CHAR will also re-shape ALL other default COMX characters.

Note that after a COLOR(x) only part of the COMX character set is re-colored (character numbers 33 until 96), this means that characters ‘on shift’ (i.e. lower case in USB CHAR(2)) will not be re-colored. SB FW is not adapted to change the COLOR command as this would cause some issues with existing software. To be able to get all characters in the right ‘COLOR’ use a USB CHAR command after the COLOR command. USB CHAR will re-shape all characters and will re-color character numbers 33 until 127 as defined in the latest given COLOR command.

## USB FLASH (x)

The COMX BASIC switches the screen output off during every SHAPE, COLOR and USB CHAR command. Since FW build 196 this has been removed. However as it changes COMX behavior (look and feel of some SW) slightly it can be switched back on by this command. Latest state is saved in NVRAM.

Switch screen flash on (x=1) or off (x=0).

Any other uneven value of x will have the same result as 1, even same as 0.

## USB LOGOTUNE (x)

Switch COMX boot tune on (x=1) or off (x=0)

Any other uneven value of x will have the same result as 1, even same as 0.

## USB BOOTMSG (x)

Switch warm start message on boot screen on (x=1) or off (x=0)

Any other uneven value of x will have the same result as 1, even same as 0.

USB GO40

Switch off 80 column card mode and switch back to normal COMX 40 column video.

If a colon (:) is used after USB GO40 any BASIC commands after the colon will be ignored.

## USB GO80 [(x)]

Without option parameter: switch on 80 column card mode.

With (x) specified: switch 80 column card auto start on (x=1) or off (x=0). No start-up screen will be shown on the 80 column output. On a reset a question for warm (W) or cold (any key except W) start-up will be shown.

Any other uneven value of x will have the same result as 1, even same as 0.

## VOLUME (x)

Set volume of BASIC sound functions (NOISE, TONE and MUSIC) with a range of 0 to 4. Where 0 is no sound and 4 is the loudest. This value is saved in NVRAM and restored at every power-up.

Note that not all SW makes use of the VOLUME setting and as such this command will not have effect for all SW. For example SW that uses 1802 out instructions to make sound (USB HIT). Also SW that on start-up use the VOLUME command will off course change this setting.

## USB SYSDISP

Show current settings for NVRAM system area.

Note: the printer settings will only be shown if the related card and printer type are connected.

## USB SYSDEF

Initiate NVRAM system area to default values:

Boot message: on

Logo tune: on

Screen editor: on

Character set: Standard characters

Clock display: off

Date format: dd/mm/yy

Time format: 24H

80 column auto boot: off

Colors: Screen 1, Color 12, Ctone 0

Volume: 4

Online: On

Flash: Off

Printer TV: off

Printer keyboard: on

Printer CNTL: normal characters

Serial printer:

- Baud rate 600

- 8 data bits

- No parity

- LF

- 2 stop bits

- CR pause 5

Note 1: The screen will be cleared if the screen editor is not active before USB SYSDEF is given.

Note 2: NVRAM Start address is NOT changed or reset, use USB NVSTART instead

# NVRAM

## USB NVLOAD

Restore NVRAM SW and user data part (F000h to F3E7h) from back-up file on the PC.

Location of the back-up file (nvram.bin) should be the ‘root’ directory as set in the COMX USB Interface SW on the PC.

## USB NVSAVE

Save NVRAM SW and user data part (F000h to F3E7h) to back-up files on the PC.

Location of the back-up file (nvram.bin) will be the ‘root’ directory as set in the COMX USB Interface SW on the PC.

## USB SYSLOAD

Restore NVRAM system area (F3E8h-F3F7h) from back-up file on the PC

Location of the back-up file (system.bin) should be the ‘root’ directory as set in the COMX USB Interface SW on the PC.

Note 1: The screen will be cleared if the screen editor is not active before USB SYSLOAD is given.

## USB SYSSAVE

Save NVRAM system area (F3E8h-F3F7h) to back-up files on the PC.

Location of the back-up file (system.bin) will be the ‘root’ directory as set in the COMX USB Interface SW on the PC.

## USB NVLIST

List content of NVRAM SW area including:

- Current defined user area (if any is defined)

- Used and free SW area

- Stored SW IDs, number of bytes used and SW name if available

Current reserved SW names:

ID	Name

1	Happiehap

2	Happiehap 2

3	Hit & run (USB HIT)

4	Space invaders (USB SPACE)

5	Eat a worm (USB WORM)

6	Get your gadget

7	GateMaster

8	COMX Dragon

9	Crossfire

10	Look before you

11	Tennismania (USB TENNIS)

NVRAM is divided in 4 areas:

F000 – Fxxx: User area, this area can be used by any user or user program. No defined format is available so any address location can be filled as desired.USB NVPOKE can be used to store data and COMX BASIC PEEK can be used to retrieve data. Fxxx is defined via USB NVSTART.

Fxxx – F3E7: SW area, this area can be used by any SW. The area is formatted so every SW program can find stored data back. USB NVPUT, NVGET, NVIGET, NVSGET, NVCLR and NVDEL can be used to store, retrieve or manipulate data to/from this area.

F3E8 – F3F7: System area, reserved for use by the SB FW.

F3F8 – F3FF: Reserved for the RTC.

## USB NVPOKE (nvram address,value)

Store value in NVRAM address location, NVRAM address range should be between F000h and F3FFh. This command will first enable NVRAM write then store the value and last reactivate NVRAM write protection again.

## [STR =] USB NVPUT (id, source, number of bytes)

Put data in NVRAM ‘SW area’ for the indicated SW id (1-255). Data that will be put into NVRAM will be from memory location ‘source’ with a length the of indicated number of bytes.

Returned string will be empty (“”) if the command is successful. If NVRAM is full the returned sting will be “NVRAM full, data not stored”.

The data stored can be retrieved via USB NVGET.

Possible return stings:

- NVRAM full, data not stored

- No rtc or nvram found, or nvram not inititiated

- Nvram write enable error

If no return string is specified, i.e. USB NVPUT (1, @4500, 4), any error will result in ‘breaking’ the program and printout of the error code.

Machine code: USB NVPUT can be called from any machine code program by calling subroutine on E019h. Before the call the following registers should be load:

R8.1: 	id

RC:  	source

R8.0: 	number of bytes

The COMX standard SEP 4 / SEP 5 should be used for the subroutine call. Content of registers: R7.0, RE and RF will be destroyed

Example:

LDI 86

PHI RC

LDI 00

PLO RC

LDI 0B

PLO R8

LDI 06

PHI R8

SEP 4	E019

SEP 5

This routine will save content of software id 6 from 8600h with a length of bh bytes.

## [STR =] USB NVGET (id, destination)

Get data from NVRAM ‘SW area’ for the indicated SW id (1-255). Data that will be received from NVRAM will be stored starting at memory location ‘destination’ with a length of the indicated number of bytes.

Returned string will be empty (“”) if the command is successful. If the requested SW id is not found the returned sting will be “Software ID not found”.

Possible return stings:

- Software ID not found

- No rtc or nvram found, or nvram not inititiated

If no return string is specified, i.e. USB NVGET (1, @4500), any error will result in ‘breaking’ the program and printout of the error code.

Machine code: USB NVGET can be called from any machine code program by calling subroutine on E01Ch. Before the call the following registers should be load:

R8.1: 	id

RC:  	destination

The COMX standard SEP 4 / SEP 5 should be used for the subroutine call. Content of registers: R7.0, RE and RF will be destroyed

Example:

LDI 86

PHI RC

LDI 00

PLO RC

LDI 06

PHI R8

SEP 4	E01C

SEP 5

This routine will load content of software id 6 to 8600h.

## [STR =] USB NVPUT (id, value <INT>, string <STR>)

Put BASIC variable data in NVRAM ‘SW area’ for the indicated SW id (1-255). The value if the INT variable and the string content will be stored in NVRAM.

Returned string will be empty (“”) if the command is successful. If NVRAM is full the returned sting will be “NVRAM full, data not stored”.

Example:

10 DEFINT A

20 A=12345

30 B$=”STORED IN NVRAM”

40 R$=USB NVPUT(2,A,B$)

The above program will store value 12345 and string STORED IN NVRAM for SW id ‘2’.

The data stored can be retrieved via USB NVIGET (INT value) and USB NVSGET (STR content)

If no return string is specified, i.e. USB NVPUT (1, A, A$), any error will result in ‘breaking’ the program and printout of the error code.

## STR  = USB NVSGET (id)

Get string content from NVRAM ‘SW area’ for the indicated SW id (1-255).

Returned string will be empty (“”) if:

- the requested SW id is not found

- no NVRAM is found or NVRAM is not initiated

## INT = USB NVIGET (id)

Get INT value from NVRAM ‘SW area’ for the indicated SW id (1-255).

Returned value will be 0 if:

- the requested SW id is not found

- no NVRAM is found or NVRAM is not initiated

Example:

10 DEFINT A

20 A=USB NVIGET(2)

30 B$=USB NVSGET(2)

## USB NVSTART (start)

Change the NVRAM ‘SW area’ start address to the specified address. This will mean that the command USB NVPUT, USB NVGET, USB NVSGET and USB NVIGET will use the NVRAM range of ‘start’ to @F3E7. Start address can range from @F000 (default) to @F3E4 and in steps of 4 bytes only.

Changing the start address will move all stored data to the new address so no data will be lost.

If the newly specified NVRAM size is smaller than the already occupied space the command will not be accepted (error code ‘Requested NVRAM size to small to fit current data’).

NVRAM space @F000 until start address is available for user data as required. It is recommended that USB NVSTART is never used in any BASIC program to avoid changing NVRAM size and setup for other users.

## USB NVCLR

Clear the complete NVRAM ‘SW area’.

## USB NVDEL (id)

Delete the data for indicated SW id (1-255) from the NVRAM ‘SW area’.

# I/O

## INT = USB JOY (1) / INT = USB JOY (2)

Read value for joystick 1 or 2 and return it to specified variable or print it.

Any other uneven value of x will have the same result as 1, even same as 0.

## INT = USB INP (port)

Read value for specified input port and return it to specified variable or print it. Port value can be 1 to 7.

## USB OUT (port, value)

Send value to specified output port. Port value can be 1 to 7, value can be a 8 or 16 bit depending on OUT port specified (port 1, 2 and 3 are 8 bit, 4, 5, 6 and 7 are 16 bit).

## USB Q (value)

Set Q=value

## INT = USB Q

Read Q value and return it to specified variable or print it.

## INT = USB EF (x)

Read specified EF flag value and return it to specified variable or print it. The x value can be 1 to 4.

# Internet Access

## USB ONLINE (x)

Switch online features on or off, on (x=1) or off (x=0).

Any other uneven value of x will have the same result as 1, even same as 0.

After USB ONLINE (0) the command USB HSWEB, USB URL, URLGET, USB URLDISP and USB BROWSER will not attempt to access any online / internet features, USB ONLINE (1) enables online features again.

Note: USB ONLINE (0) can also be used to disable games to sync to the high score server. Also when using the COMX / SB without connection to a PC, USB ONLINE (0) will eliminate any additional delays when running the build in games.

## [STR=] USB URL,”url”

## [STR=] USB URL (link number)

Set url string to be used in USB URLGET (screen). When the url command is used with a string the indicated string is used to set the URL address. If a link number is given the link number will used to set the URL address according to the link specified on the current screen. So USB URL (3) will set the URL address to the 3rd link currently displayed on the screen.

If the command is successful the optional return string will contain the requested URL for USB URL,”url” and will be empty (“”) for USB URL (link number).

Possible error return strings:

- USB transfer timeoutb

- USB transfer error

- Online features disabled

## [STR=] USB URLGET (screen)

Fetch screen number x from the PC based on the previously set url. If there is no data in the requested screen the error code ‘No more data found’’ will be returned.

Optional return string will be empty (“”) if the command is successful. Possible error return strings:

- USB transfer timeout

- USB transfer error

- Online features disabled

- Network error

- No more data found

- URL not found

## USB URLDISP

Display latest fetched URL screen on COMX.

During execution of this command USB CHAR(7) will be executed to set lower case ‘default’ and upper case characters on ‘SHIFT’.

Screen color and character color will follow information as specified in the fetched URL screen.

Warning: if no valid data is loaded via USB URLGET a USB URLDISP command will most likely crash the COMX due to an invalid OUT 3 command based on invalid data.

## USB BROWSER [,”url”]

Open specified url string in a text browser, if no url is specified the default ‘home page’ is opened.

Key commands - valid with magenta (or no) cursor:

- Movement:

  - Joystick down: 		Move cursor to next topic / link

  - Joystick up: 		Move cursor to previous topic / link

  - Joystick right or CR: 	Follow selected link

  - Joystick left:		Return to previous topic

- Scrolling:

  - + or Space: 		Scroll down to next page

  - -: 			Scroll up to previous page

- Other:

  - CNTL B:		Return back to BASIC

  - G:			Go to specific URL. 
                                       Latest selected URL will be specified as default.

  - H:			Go to home page

  - SHIFT H:		Set current page as home page

  - 0-9:			Go to bookmark 0 to 9

  - SHIFT 0-9:		Set current page as bookmark 0 to 9

  - ?:			Show help page

Key commands - valid with yellow or diamant cursor (edit mode):

- Movement:

  - Joystick down: 		Move cursor to next topic / link or line

  - Joystick up: 		Move cursor to previous topic / link or line

- Other:

  - CNTL B:		Return back to BASIC

  - CR or CNTL T:		Store form text or URL

Key commands - valid with yellow cursor (edit mode):

- Movement:

  - Joystick right : 		Cursor to right

  - Joystick left:		Cursor to left

- Other:

  - CNTL Q:		Quit ‘go to’ URL feature and return to text browser

Default home page and bookmarks:

Homepage: Emma 02

Bookmark 0: Super Board - High Scores

Bookmark 1: AVI - COMX 35

Bookmark 2: AVI - Super Board

Bookmark 3: Emma 02 - COMX 35

Bookmark 4: Emma 02 - COMX BASIC

Bookmark 5: Elf/1802 Emulation

Bookmark 6: COSMAC ELF

Bookmark 7: Spare Time Gizmos

Bookmark 8: AVI - COSMAC VIP

Bookmark 9:

HTML ASCII characters:

HTML characters 161 to 255 will be shown as long as not more than 31 of these characters need to be shown on one COMX screen at the same time. If more than 31 characters are needed an X will possibly be shown for the 32nd and onwards characters. This is depending on how many ‘regular’ characters are shown on the same screen.

If any input checkboxes or radios are used 4 characters from the available 30 characters per COMX screen will be reserved.

Reserved shapes:

0: Empty space in screen editor functions

1 – 30: used for <comxshape> and &shapeX; tags. For more info see COMX HTML tag section.

31: X used for special characters that can’t be displayed

127: Cursor

COMX HTML tags:

<comx shapeX=”112233445566778899”>

Shape character with identified number X (1-126), where 11 is the hexadecimal shape code for line 1, 22 for line 2 etc.

Characters 1 to 30 will work as any HTML ASCII character and can be shown by using &shapeX; where X is 1 to 30.

Characters 32 to 126 are the normal ASCII characters and a re-shape via <comx shapeX> will result in changing the shape for that character until another <comx shapeX> for the same character is done.

Note that the USB BROWSER command uses a USB CHAR (7) so lower and capital case characters are reversed!

Example:

<comx shape65="FFFFFFFFFFFFFFFFFF">a

Will show a cyan colored block instead of all characters a

Example:

<comx shape1="FFFFFFFFFFFFFFFFFF">&shape1;

Will show a cyan colored block for every &shape1; that is specified in the HTML file.

&shapeX;

Used to show shape characters 1 to 30.

<comx char=”format”>

When format is:

High or white: change character mode to use characters 128-255. For all regular characters this means: show in color white which is the same as is used for URL links.

Low or cyan: Change character mode to use characters 0-128. For all regular characters this means: show in color cyan which is the same as is used for normal text.

<comx screen=”color”>

Change COMX background color, where color can be either a number or the color written in text:

1: Black

2: Green

3: Blue

4: Cyan

5: Red

6: Yellow

7: Magenta

8: White

Note: when using the comxscreen tag for a page that page will also be shown with default comxcolor (12) and comxctone (0) settings. That is unless also comxcolor and comxctone tags are specified.

<comx color=”colormix”>

Change COMX character color, where colormix can be a number from 1 to 12:

|  | Normal text / <comxcharlow> | URL links / <comxcharhigh> |
| --- | --- | --- |
| 1 | Black | Green |
| 2 | Red | Yellow |
| 3 | Blue | Cyan |
| 4 | Magenta | White |
| 5 | Black | Blue |
| 6 | Red | Magenta |
| 7 | Green | Cyan |
| 8 | Yellow | White |
| 9 | Black | Red |
| 10 | Blue | Magenta |
| 11 | Green | Yellow |
| 12 | Cyan | White |

These color changes will be effective for all standard ASCII characters including characters 161-255. However when a character is changed by <comxshape> that character will NOT follow the coloring above but as defined in the shape commando following the definition below:

|  | Red | Blue | Green |
| --- | --- | --- | --- |
| 1-4 | CCB0 | CCB1 | PCB |
| 5-8 | CCB0 | PCB | CCB1 |
| 9-12 | PCB | CCB0 | CCB1 |

CCB0: Bit 6 as defined in character shape

CCB1: Bit 7 as defined in character shape

PCB: bit 7 of character number (see comxcharlow/comxcharhigh tags)

Note: when using the comxcolor tag for a page that page will also be shown with default comxscreen (1) and comxctone (0) settings. That is unless also comxscreen and comxctone tags are specified.

<comx ctone=”format”>

Change COMX color format, where format can be: 0 / color or 1 / gray. Either a number or text is allowed.

Note: when using the comxctone tag for a page that page will also be shown with default comxscreen (1) and comxcolor (12) settings. That is unless also comxscreen and comxcolor tags are specified.

## USB EMAIL

Start the COMX Email editor.

Key commands - valid with magenta (or no) cursor:

- Movement:

  - Joystick down: 		Move cursor to next topic / link

  - Joystick up: 		Move cursor to previous topic / link

  - Joystick right or CR: 	Follow selected link

- Scrolling:

  - + or Space: 		Scroll down to next page

  - -: 			Scroll up to previous page

- Other:

  - CNTL B:		Return back to BASIC

  - ?:			Show help page

Key commands - valid with yellow cursor (edit mode):

- Movement:

  - Joystick down: 		Move cursor to next topic or line

  - Joystick up: 		Move cursor to previous topic or line

  - Joystick right : 		Cursor to right

  - Joystick left:		Cursor to left

- Other:

  - CNTL B:		Return back to BASIC

  - CR or CNTL T:		Store form text

  - CR in message field:	Go to next line

Aliases can be used in the ‘To’ field if they are defined in the PC SW. See also chapter ‘Online settings’.

## [STR=] USB HSWEB

Synchronize latest high scores with the Super Board high scores server (http://www.comx35.com/comx35sbhs/hs2.php). Scores for the software IDs as listed under USB NVLIST will be synchronized but only if a score is already stored in NVRAM. If no score is stored no synchronization for that game will be done; to store a score just play the game once (make sure to play a game that is adapted to include NVRAM high score code).

Player name and location will be taken from the USB PC SW. Except for Happiehap, Happiehap 2 and Get your gadget where the player name will be used from the game itself.

Optional return string will be empty (“”) if the command is successful. Possible error return strings:

- USB transfer timeout

- USB transfer error

- Network error

- Server error

- Online features disabled

If no return string is specified, i.e. USB HSWEB, any error will result in ‘breaking’ the program and printout of the error code.

Machine code: USB HSWEB can be called from any machine code program by calling subroutine on E013h.

The COMX standard SEP 4 / SEP 5 should be used for the subroutine call. Content of registers: R7.0, R8, RC, RE and RF will be destroyed

# Turbo Tape

## USB TLOAD[+]

## USB TSAVE[+]

## USB TDLOAD[+]

## USB TDSAVE[+]

F&M Turbo tape routines work exactly like BASIC save/load commands except much faster. The '+' versions are improved versions resulting in different wav formats. The wav files created with the regular versions can be loaded with the regular and '+' versions. Wav files created with the '+' versions are not loadable with the regular versions.

# Printer

## USB PON

Turn the printer on with CNTL characters suppressed.

This command will first search for a standard printer card, if found it will be selected and the printer output will be activated. If no standard printer card is found a search will be done for the thermal printer card.

The printer output can be switched off via USB PROFF. Also note that most USB and DOS commands will switch off the printer output except for:

- USB CAT

- USB VER

- USB CD

- USB HEX

- USB BIN

- USB NVLIST

- USB HELP

- USB SYSDISP

- USB HISTORY

## USB POFF

Turn printer output off

## USB PTV (x)

Select printer setting to enable or disable TV output during ‘printer on’. x=0 (default) no output will be done to the TV screen after USB PON, x=1 output will be done to both TV and printer after USB PON.

If output to TV is selected USB PON will also temporarily switch the clock off until the printer is switched off again.

## USB PCNTL (x)

Switch printer CNTL character suppression on (x=1, suppressed; normal characters) or off (x=0, hex values). Set value will be stored in NVRAM and used for the USB PON, USB PTVON, USB PTEST, USB PLIST and USB PPRINT commands.

Any other uneven value of x will have the same result as 1, even same as 0.

## USB PKB (x)

Select keyboard output setting to the printer. x=1 (default) keyboard output will be send to the printer, x=0 no keyboard output will be send to the printer

## USB PMEMDUMP (start, end)

Start memory dump routine and send result to printer.

If memory location C000h to DFFFh is included the content of the current selected slot and bank will be printed. To select a different slot use the CARD Sx command, to select a different bank use the CARD Bx command.

## USB PTEST

Start printer test routine.

## USB PSET

Set serial printer configuration. The set configuration will be stored in NVRAM and used for USB PON, USB PMEMDUMP, USB PLIST, USB PPR and USB PPRINT commands.

## USB PLIST

Same as LIST command but output is send to the printer.

## USB PPR / USB PPRINT

Same as PRINT command but output is send to the printer.

# F&M Monitor

## USB MON

Start F&M Monitor!

Note that the ‘Program start’ value is save in regular RAM on location 4403h/4404h so that the value is save in the current loaded program and saved within the USB PSAVE command. This also means the ‘Program start’ value should never be defined as a value below 4405h as that will crash the monitor when using the CNTL I/D features.

Machine code: The register read function can be called from any machine code program by calling subroutine on E016h. The COMX standard SEP 4 / SEP 5 should be used for the subroutine call. Content of registers RF will be destroyed.

USB DMON

Start F&M Disk Monitor

Note F&M Disk Monitor uses some BASIC RAM, USB DMON will save these RAM areas to (RAM) bank 15 and restore to original values at exit to BASIC (key 3).

# Games

## USB TENNIS

Start Tennismania.

Note Tennismania uses some BASIC RAM, USB TENNIS will save these RAM areas to (RAM) bank 15 and restore to original values at exit to BASIC (key CNTL B).

High scores are saved in NVRAM with SW ID=11.

## USB SPACE

Start Space invaders.

Additional key functions compared to original game:

CNTL B: Return to BASIC

S: Toggle sound on / off

High score and sound setting are saved in NVRAM with SW ID=4.

Note Space invaders uses some BASIC RAM, USB SPACE will save these RAM areas to (RAM) bank 15 and restore to original values at exit to BASIC (key B).

## USB WORM

Start Eat a worm.

Additional key functions compared to original game:

CNTL B: Return to BASIC

S: Toggle sound on / off

This version of the game does not support the ‘bonus’ and ‘level’ features as in the original. However it does support two new features instead:

- WALL counter, which counts the number of worms that need to be eaten until a wall forms

- Speed increase, the longer you play the faster your snake will run

High score and sound setting are saved in NVRAM with SW ID=5.

Note Eat a worm uses some BASIC RAM, USB WORM will save these RAM areas to (RAM) bank 15 and restore to original values at exit to BASIC (key B).

# COMX DOS to PC

## USB IMGTEST,”filename”

Check format of image file on PC and show if it needs a floppy disk formatted to single/double sided and single/double density.

## USB IMGTODISK,”filename” [/DR]

Copy a disk image file from the PC to a floppy disk. PC filename should have extension .img, however no extension should be given in the USB command. During the image copy the disk side and track currently being written is shown on the screen.

Example:

USB IMGTODISK,”GAMES”

will put the games.img image on the current floppy disk.

Note that the destination floppy disk HAS TO be formatted with DOS INIT with the same parameters as the disk image. See USB IMGTEST to find out what format is needed.

ESC key (long press) will stop the command but note that destination disk in this case will not be usable.

## USB DISKTOIMG,”filename” [/DR]

Copy a floppy disk to a disk image file on the PC. PC filename will get extension .img, however no extension should be given in the USB command. During the image copy the disk side and track currently being written is shown on the screen.

Example:

USB DISKTOIMG,”GAMES”

will put the current floppy disk content to an image called games.img.

ESC key (long press) will stop the command but note that destination image in this case will not be usable.

# Graphics

Most commands described in this chapter were added in FW build 195, released July 2016. With the exception of commands USB TV, USB DHEIGHT and USB DWIDTH.

## USB GRAPH

Change back to normal text screen, this will include a clear screen and re-shape of current selected character set. Note USB GRAPH (except for the clear screen) is executed automatically when a program ends, this to avoid a ‘hanging’ COMX as no command entry is possible in the ‘graphic' modes.

## USB GRAPH (graphic screen)

Graphic screen values range from 0 to 7 where:

Bit 0 = 0: Characters size 6*9 or 6*8 pixels

Bit 0 = 1: Characters size 6*16 pixels

Bit 1 = 0: Normal pixel size

Bit 1 = 1: Double width / double height pixels

Bit 2 = 0: PAL resolution (6*9 character size, 108 pixel screen height),

Bit 2 = 1: NTSC resolution (6*8 character size, 96 pixel screen height)

If bit 0=1 then setting bit 2 has no effect and the character size will be 6*16 with a screen height of 108 pixels. Note that these cases (graphic screen 5 and 7) are used for extended / different versions of graphic screen 1 and 3.

For all graphic screen variants (except 7) the complete defined area will NOT be usable. This is because not all pixels can be addressed individually (max 127 blocks of 6*16 pixels is possible) due to the fact that USB GRAPH uses 127 characters to simulate the graphic screen. The 127 characters can’t fill any of the graphic screen resolution. When no more characters are available USB PLOT, LINE, CIRCLE and ELLIPSE will just stop working; i.e. nothing is plotted.

Graphic screen 0, 2, 4 and 6 allow use of PRINT and CPOS features but PRINTed text will be re-shaped if too many USB PLOT, LINE, CIRCLE or ELLIPSE commands are executed.

Graphic screen 0:

(normal text screen, including limited plot feature like PECOM 64:

X: 0-227, Y: 0-107

Character size: 6*9 pixels

Pixel size: normal

Note: First screen line and first 2 character columns are not used, so USB PLOT (0, 0, 8) will plot in the bottom left hand corner of the character in CPOS (12,2), i.e. line 13 and character 3.

Graphic screen 1:

X: 0-239, Y: 0-215

Character size: 6*16 pixels

Pixel size: normal

Note: The last line on the screen will use character size 6*8.

Graphic screen 2:

X: 0-119, Y: 0-107

Character size: 6*9 pixels

Pixel size: Double width / double height

Graphic screen 3:

X: 0-119, Y: 0-107

Character size: 6*16 pixels

Pixel size: Double width / double height

Graphic screen 4:

X: 0-227, Y: 0-95

Character size: 6*8 pixels

Pixel size: normal

Note: This is an NTSC version of graphic screen 0. When using this screen on a PAL COMX the first 3 character lines (16 pixel lines) will be repeated on the bottom of the screen.

Graphic screen 5:

X: 0-239, Y: 0-207

Character size: 6*16 pixels

Pixel size: normal

Note: This is more or less the same as graphic screen 1 except the last line on the screen is never used. This makes USB PLOT (0, 0, 8) start 8 pixels higher compared to graph 1. As the last line on graphic screen 1is only 8 pixels high graphic screen 5 in a way allows more pixels to be drawn but on a smaller area.

Graphic screen 6:

X: 0-119, Y: 0-95

Character size: 6*8 pixels

Pixel size: Double width / double height

Note: This is an NTSC version of graphic screen 2. When using this screen on a PAL COMX the first 12 pixel lines will be repeated on the bottom of the screen.

Graphic screen 7:

X: 0-107, Y: 0-107

Character size: 6*16 pixels

Pixel size: Double width / double height

Note: This is more or less the same as graphic screen 3 except the first and last 'column' of the screen are not used. This makes USB PLOT (0, 0, 8) start 6 pixels to the right compared to graphic screen 3. Due to this fact all (defined) positions of the screen can be filled by using 126 characters, meaning USB PLOT will never stop working as the characters never 'run out'.

## USB PLOT (x, y, color)

Plot one pixel on position X, Y. Note that 0, 0 is the bottom left hand corner of the screen (so NOT like CPOS).

Color identifies the color of the pixel (1=black to 8=white), following the COMX SCREEN color numbering. Note that the last color ‘plotted' can affect color of pixels already on the screen. This because only one pixel color is possible for every 6 pixels in an horizontal ‘row' (and of course the screen background color), also on every character (6*8, 6*9 or 6*16) only color 1 to 4 or 5-8 can be displayed simultaneously. The last use USB PLOT color will change colors on the same line of 6 pixels and on the same character if needed.

## USB PLOT (x, y, color, character)

Plot character on position X, Y. Note 0, 0 is the bottom left hand corner of the screen.

Color identifies the color of the pixel (1=black to 8=white). Colors have the same limitation as for USB PLOT.

Character number is drawn as defined in the standard COMX ROM character set, where ‘A' is 65. However lower case characters are printed if character number is between 97-122 as in a standard ASCII definition.

Character is drawn ‘down' from x, y; so x, y is the top left corner of the character. DOS INIT

## USB LINE (x, y, color, x2, y2)

Plot a line from position X, Y to X2, Y2. Note 0, 0 is the bottom left hand corner of the screen.

Color identifies the color of the pixel (1=black to 8=white). Colors have the same limitation as for USB PLOT.

## USB CIRCLE (x, y, color, radius)

Plot a circle with the centre at position X, Y and radius. Note 0, 0 is the bottom left hand corner of the screen.

Color identifies the color of the pixel (1=black to 8=white). Colors have the same limitation as for USB PLOT.

## USB ELLIPSE (x, y, color, a, b)

Plot an ellipse with the centre at position X, Y, horizontal radios a and vertical radius b. Note 0, 0 is the bottom left hand corner of the screen.

Color identifies the color of the pixel (1=black to 8=white). Colors have the same limitation as for USB PLOT.

## USB DCHAR (state)

Double character lines:

Bit 0 = 0: default 9 (or 8 on NTSC) character lines

Bit 0 = 1: 16 character lines

Bit 1 = 0: do not clear shape lines 9 (or 8 on NTSC) to 16

Bit 1 = 1: clear shape lines 9 (or 8 on NTSC) to 16

USB DCHAR (1) or USB DHAR (3) will almost double the graphic capacity from 128 characters with 9 (or 8 for PAL) lines to 128 characters with 16 lines. This mode is giving similar resolution as when using USB GRAPH with graphic screen bit 0 set to 1.

In double character line mode the lines 10 to 16 will show random shapes until changed via the USB SHAPE command u3nless bit 1 is set to 1 with USB DCHAR (3). Clearing shape lines 9 to 16 will also disable the screen editor so after any USB DCHAR (3) on return to BASIC prompt a USB GRAPH will be executed to reset screen and shapes to normal like is done after USB GRAPH (x).

Note that the COMX and the Screen editor will also not be able to handle doubling of the character lines very well when using USB DCHAR (1). Half of the lines will not be shown anymore. To return back to normal give the USB DCHAR command with state=0.

## USB SHAPE (character, shape string)

Extended SHAPE command where the shape string can consist of a string with 16 bytes to allow ‘shaping’ of character line 10 (or 9 on PAL) up to 16. This command is added so it can be used to ‘shape’ line 10 to 16 when using USB DCHAR (1).

Note that using USB SHAPE in combination with the screen editor can cause some input to be disabled.

For example after:

USB SHAPE (65,”00112233445566778899AABBCCDDEEFF”)

Input of the character A will become impossible. Meaning no SHAPE command or any command using character ‘A’ will be accepted by the screen editor. Only a reset or execution of the USB GRAPH command will resolve this issue. Because of this it is probably good practice to start any program using USB SHAPE with a USB LINE command so the screen editor is disabled. At the end of program execution a USB GRAPH and USB SCREEN will reset the screen editor to default settings. Reason for this issue is because the screen editor uses character line 10 to identify the character number. So character 65 has a line 10 shaped as 64 or 41 hexadecimal. This is used to read what character is located where because the page memory is not readable but the character memory is on a COMX.

## USB TV (state)

Turn TV screen on (1) or off (0).

This command can be used to get a picture or text shown on screen very fast by first turning the TV off  with USB TV(0), then printing the screen and at the end turning the TV back on with USB TV(1).

Note USB TV(0) will also disable the keyboard!

## USB PPOKE (page RAM address ,value)

Store value in CDP1870 page RAM address location, page RAM address range is between 0 and 3FFh. Specified address will always be converted to a value within this range. So a USB PPOKE on address 400h will result in a USB PPOKE on address 0.

Page RAM location 0 is not necessarily the top left hand corner of the screen as this is depending on scrolling done since restart. To find the current top of screen location use value stored on address 4195h and 4196h.

Example:

10 P=PEEK(@4195)*256+PEEK(@4196)

20 USB PPOKE (P, 65)

Will store character ‘A’ somewhere in the page RAM which on a COMX screen will show an ‘A’ on the top left corner of the screen.

The main advantage of using USB PPOKE instead of a PR CHR$() is that with USB PPOKE it is possible to put any character on the screen including characters 10 (Ah) and 13 (Dh).

## USB CPOKE (address, value) / USB CPOKE (character, line, value)

Store value in CDP1870 character RAM on specified address, character RAM address range is between 0 and 7FFh. Specified address will always be converted to a value within this range. So a USB CPOKE on address 800h will result in a USB CPOKE on address 0.

CDP1870 character RAM is build up of 16 bytes per character starting with character 0 and using 1 byte per character line.

One USB CPOKE command will change the shape of 1 line of a character.

Example:

USB CPOKE (1040,#FF)

This will shape the top line of character ‘A’ to a line.

1040 is character 65 (‘A’) multiplied by 16 (16 lines per character)

The following formula can be used to calculate the character RAM address: character_number*16+line_number

For convenience a second USB CPOKE command is available where character number and line can be specified. So USB CPOKE (65, 0, #FF) is the same as USB CPOKE (1040,#FF).

## INT = USB CPEEK (address) / INT = USB CPEEK (character, line)

Similar to USB CPOKE however will read a value from the CDP1870 character RAM on specified address, character RAM address range is between 0 and 7FFh. Specified address will always be converted to a value within this range.

For convenience a second USB CPEEK command is available where character number and line can be specified. So A = USB CPEEK (65, 0) is the same as A = USB CPEEK (1040).

## USB DWIDTH (state)

Set pixel width to double size. State 1 = double and 0 = normal.

Note that the COMX and the screen editor will not be able to handle double pixel width very well. Half of the lines will not be shown anymore. To return back to normal pixel width and height press CNTL S (or give the applicable command with state=0).

Note that on FW version 1.91 and before: When using CPOS or USB POS when double width is active the first line on the screen will be line 0 and column 0 to 19, the second line will also still be line 0 but column 20 to 39. From FW version 1.92 this is corrected so CPOS(1,0) is the first location of the second line.

## USB DHEIGHT (state)

Set pixel height to double size. State 1 = double and 0 = normal.

Note that the COMX and the screen editor will not be able to handle double pixel width very well. Half of the lines will not be shown anymore. To return back to normal pixel width and height press CNTL S (or give the applicable command with state=0).

# REM adaptation

Commands described in this chapter were added in FW build 195, released July 2016.

## USB LIGHTRM line

Change color of text in REM command on indicated line from output color (default cyan) to input color (default white). Colors cyan and white are depending on which COLOR combination is used.

To return to normal output color: execute the USB LIGHTRM command a second time for the same line number.

## USB HIDERM line

Hide line number of indicated REM line. The text following the REM command will overwrite the line number and REM command text.

To return to normal output: execute the USB HIDERM command a second time for the same line number.

Examples:

10 REMABCDEFG

20 REM---REM Text

30 REMXX

After USB HIDERM will show:

ABCDEFG

---REM Text

XX REM

Obviously when using the Screen editor the hidden REM lines cannot be edited when ‘listed’’ on the COMX screen. Also the EDIT command when the LINE editor is active will not work correctly. To edit these lines return to normal output with a second USB HIDERM.

# RENUMBER extension

Commands described in this chapter were added in FW build 196, released July 2016.

## RENUMBER start, end [,line] / RENUMBER [line]

With the new extended RENUMBER command it is possible to renumber only part of the BASIC code by specifying the start and end address of the part to be renumbered. Note that the address specified as ‘end’ will NOT change number to make it easier to renumber subroutines.

Examples:

1000 REM Subroutine 1

1005 REM some code

2000 REM Subroutine 2

RENUMBER 1000,2000

This will result in:

1000 REM Subroutine 1

1010 REM some code

2000 REM Subroutine 2

Optional 3rd parameter ‘line’ specifies the line increment which if omitted will default to 10.

If during the RENUMBER the COMX detects that the new renumbering doesn’t fit between specified ‘start’ and ‘end’ it will automatically decrease the increment with 1.

The extended RENUMBER command will also handle BASIC line numbers >65280 which were not handled in the original command. Note however that COMX BASIC does have some other limitations with line numbers >65280 so it is recommended not to use any line number between 65280 and 65535.

# Slot And Card Access

## CARD B (x) or CARD Bx

Select ROM or RAM bank in slot 4, where x=0 to 14.

Bank 0-7 are used for USB FW and bank 8 to 14 for 7 8K RAM banks.

Note that selecting bank 15 will not be accepted in this command. This is because RAM bank 15 is reserved for use by the SB FW and when overwritten will cause the COMX to behave incorrectly.

() is optional for hard coded values, however if variables or calculations are used as ‘x’ () are mandatory. E.g. B=7: CARD B(B) and CARD B7 are correct but B=7:CARD BB is invalid.

## [INT =] CARD B

Return the current selected bank, possible return values are bank 0 to 15.

If CARD B is used without preceding variable or PRINT the bank value will be printer to the screen.

## CARD S (x) or CARD Sx

Select slot x, where x=1 to 4.

() is optional for hard coded values, however if variables or calculations are used as ‘x’ () are mandatory. E.g. S=2: CARD S(S) and CARD S2 are correct but S=2:CARD SS is invalid.

CARDS0 and CARDS4 also have the same behavior as the USB command.

## INT = CARD S

Return the current selected slot, possible return values are slot 1 to 4.

## [INT =] CARD F (x) or [INT =] CARD Fx

Find and select card type x. Optional return value is the selected slot with card type x. If the card type is not found 0 is returned.

Known types:

1: Standard printer card

2: Thermal printer card

3: Floppy disk card

4: 80 Column card

5: EPROM programmer (I have never seen this one!)

6: Network card

33: USB FW, always slot 4

() is optional for hard coded values, however if variables or calculations are used as ‘x’ () are mandatory. E.g. F=1: CARD F(F) and CARD F1 are correct but F=1:CARD FF is invalid.

## USB

Select the SB card (slot 4 and bank 0).

Commands CARDS0 and CARDS4 also have the same behavior as USB.

# COMX DOS

DOS BOOT

Force re-boot of COMX DOS 1.4 from ROM.

## DOS INIT

Formats a disk.

## DOS STARTUP

Formats a disk like the INIT program however with an F&M startup boot sector which will attempt to load and run a program called 'STARTUP' when DOS is booted from this disk after a power up (like with DOS NEW).

Note: After a DOS STARTUP command the next DOS command will fail with an error message ‘File not found in directory’. This is caused by the fact that DOS is booted after every DOS STARTUP and DOS INIT, in this case the DOS boot cannot find the ‘STARTUP’ file on the disk and will report that in an error message. It is recommended to always give a DOS NEW after the DOS STARTUP is finished to ‘flush’ out the first boot including the file not found error.

Also remember that DOS is only booted on a DOS command from disk after a power-up and or after DOS INIT / STARTUP. DOS BOOT boots from ROM and as such will not use the STARTUP function.

Example:

DOS STARTUP

COMX DOS V1.4

COPYRIGHT BY  COMX – 1984

INSERT FORMAT DISK THEN PRESS ANY KEY

ARE YOU SURE ? (Y/N) Y

DRIVE NO. (1 OR 2) ? 1

DOUBLE TRACK DENSITY ? (Y/N) N

SINGE(1) OR DOUBLE(2) SIDE ? 2

ARE YOU SURE ? (Y/N) Y

DISK NAME (MAX.8 CHARS) ? TEST

DATE (DD-MM-YY) ? 05-07-13

READY

DOS NEW

F&M STARTUP © 1986

File not found in directory

READY

10 PRINT “STARTUP PROGRAM”

DOS SAVE,”STARTUP”

READY

## DOS LABEL,”diskname” [/DR]

Change the disk name to specified string. Maximum 8 characters can be specified for the diskname.

DOS DATE,”date” [/DR]

Change the disk date to specified string. Maximum 8 characters can be specified for the disk date. Any date format will be allowed.

## DOS LOCK [,”filename”] [,D] [,W] [/DR]

Lock specified software on the disk. Option D is used for the delete protection and option W for write protection. /DR is the drive number (1 or 2). When no filename is specified all software on the disk is locked according to remaining options. When no D or W is specified both protections will be set, when no /DR is specified drive 1 will be used.

## DOS UNLOCK [,”filename”] [,D] [,W] [/DR]

Unlock specified software on the disk. Option D is used for the delete protection and option W for write protection. /DR is the drive number (1 or 2). When no filename is specified all software on the disk is unlocked according to remaining options. When no D or W is specified both protections will be removed, when no /DR is specified drive 1 will be used.

## DOS DISKCOPY

Make an exact copy of a disk including a format/initialization of  the destination disk before copy begins.

Note this command will destroy content of (RAM) bank 13 and 14. This is done to save BASIC RAM content from address @5000 to @9FFF which is used by the DISKCOPY command. BASIC RAM is only restored if the command is successfully executed.

## DOS FILECOPY

Make a copy of a specific file.

Note this command will destroy content of (RAM) bank 13 and 14. This is done to save BASIC RAM content from address @5000 to @9FFF and @AC00 to @AFFF which is used by the FILECOPY command. BASIC RAM is only restored if the command is successfully executed.

# Other Commands

## USB VER

Show version, copyright and date information.

## USB OLD [,defus address]

Restore ‘old’ BASIC program. When the optional defus address is specified the program at the specified address will be recalled. If no address is specified the program at default defus address of 4400h will be restored.

If a recall is done for defus address 4400h the restore will only be successful if the original program started with 10 REM.

## USB HELP [,“command”]

Show command format for specified command or any command that contains the specified string. For example USB HELP “USB” will show all USB commands. If more than 24 lines of command help is shown the command will pause until a key is pressed, if Q is pressed help will quit.

If the command string is equal to a “*” all supported BASIC commands will be shown.

If the command string is omitted a short explanation and format for help will be shown.

## USB HISTORY

Show last 8 commands (including USB HIST) which can be ‘recalled’ by using CNTL R, see also Screen Editor help.

## STR = USB HEX (value)

Return the hexadecimal value of the variable or number specified. Max value is 8388607 or hexadecimal 7FFFFF.

## STR = USB BIN (value)

Return the binary value of the variable or number specified. Max value is 8388607, binary values are returned in either 8 bit, 16 or 24.

## INT = USB POS (row, column)

Return the ASCII value of the character on screen position row / column. Row = 0 and column = 0 represent the top left corner of the screen.

## USB MEMDUMP (start, end)

Start memory dump routine and send result to screen.

If memory location C000h to DFFFh is included the content of the current selected slot and bank will be printed. To select a different slot use the CARD Sx command, to select a different bank use the CARD Bx command.

# Screen Editor

Joystick: move cursor

CNTL D: Delete character at cursor and shift rest of line left

CNTL S: Clear the screen and switch character size back to normal

CNTL I: Insert space at cursor and shift rest of line right

CNTL R: Repeat last line, a total of 8 lines are kept in a buffer if a RAM chip is installed in the SB

CNTL X: Copy line of current cursor position to ‘copy’ buffer, the buffer is 96 characters long. If the cursor is on a line with more than 96 the cursor will be moved to the position after the characters that are copied to the buffer. If no RAM chip is installed in the SB the CNTL R buffer will be used.

CNTL V: Paste the content of the ‘copy’ buffer to the current cursor position

CNTL E: Move cursor to end current line

CNTL W: Wipe current line from cursor position

SPACEBAR during LISTING: Pause LIST function until next SPACEBAR press

Note 1: Some software, like the original version of the F&M Monitor+, might not be fully compatible with the screen editor and when giving control back to BASIC, after the program is ended, the screen looks empty but at every return error: ‘Line buffer overflow’ is given. To solve this just press CTRL S to really clear the screen.

Note 2: Some software, like Kleiduiven Schieten, Torens van Hanoi, Ijskikker and F&M Schaak might not be fully compatible with the screen editor because they use the character 0 for a different shape. In this case the screen will be filled with funny shaped characters instead of spaces. To avoid this problem you can switch off the screen editor by using USB LINE.

Note 3: Some software, like Killerwatt might not be fully compatible with the screen editor and will cause the game to hang.

# Other features

- Saved in NVRAM and initiated at startup:

  - Clock display on / off

  - Boot message (W = WARM START) on / off

  - Selected character set (USB CHAR)

  - 80 Column auto start-up (USB EIGHTYCOL)

  - Logo tune (USB LOGOTUNE)

  - Line editor / screen editor selection

  - Time and date format

  - Volume

  - Printer settings

  - Online status

  - SHAPE, COLOR and USB CHAR screen flash

# Bug fixes

  - Red dot in shape of exclamation mark

  - Temporary stack 4FFFh changed to BDFFh to avoid change of RAM memory locations 4FF7h-4FFFh during restart

  - Typing ’10 TOUT’ on clean startup hanging fixed, TOUT is replaced by USB anyway but still ’10 USB’ will not cause any hanging either.

  - Crash on typing READ x when no DATA statement is available in the loaded BASIC program.

  - Bug fixed in F&M expansion ROM where CARDS caused a crash

  - Bug fixed when 65535 line number is typed

  - Fixed COMX BASIC bug that crashed EDIT x where x was not an integer value like EDIT (10

  - Corrected error code when typing SHAPE without parenthesis

# Extra Features

- When 80 column card is plugged in it is possible to start directly in 80 column mode

- Press ‘W’ on start-up to boot with ‘warm’ start, i.e. BASIC will not be reset. Plus added Warm start text on logo screen

- Press ‘C’ on start-up to show copyright screen

- Extended text on 4th boot screen including longer delay

- Extended BASIC start-up message

- All (x) can be replaced by basic expressions like (1+4) or (A) etc

- All string values can be replaced by string expressions like A$, A$(1), A$+B$, MID$(A$,1,4) etc

- Changed the expansion ROM error code ‘ERROR’ or ‘SYNTAX ERROR’ to ‘Syntax error in CARD statement’. Also using DOS will give error ‘NO DISK CARD’ if no disk card is found. This was removed in the F&M expansion version to save space.

- All ERR CODE numbers replaced by text including BASIC, DOS, F&M BASIC and USB error codes

- All ERR CODE text and HELP text will be capitalized correctly independent of used USB CHAR

- Added line of spaces after ‘READY’ prompt

- Changed EDIT x to show line number only in screen editor mode to simplify editing as well as to avoid issues that caused EDIT not to work correctly in screen edit mode

- Moved shape ‘&’ 1 line up

- Moved top line for shape ‘#’ 1 line lower

- Added a call to ‘DOS NEW’ on startup (only if DOS was booted before reset), so no DOS NEW needs to be given manually anymore

- Keyboard is cleared after every ‘ESC’ press so no unwanted characters show up at the READY prompt

- Command entry in ‘SHIFT’ characters is allowed in screen editor with CHAR (2) or (3) active. All commands are stored as ‘normal’ characters. i.e. in capitals for CHAR (2) and lower case for CHAR (3).

- Map joystick 1 values to the COMX keyboard. This will allow BASIC SW and in some cases machine code SW (only if BASIC key read routines are used) to be used with joystick 1. Fire key is mapped to space bar and up/down/left/right to the build in joystick. This function only works when slot 4 is selected and active.

# APPENDIX A – MEMORY MAP

## COMX & Super Board Memory MAP

| Address | Original COMX 35 | COMX + Super Board |
| --- | --- | --- |
| 0000 - 3FFF | COMX BASIC ROM | SB BASIC ROM |
| 4000 - 43FF | BASIC System Parameters | BASIC System Parameters |
| 4400 - BDFF | USER RAM | USER RAM |
| BE00 - BFFF | Reserved for use by expansion cards | Reserved for use by expansion cards and used by SB |
| C000 - DFFF | Reserved for 4 expansion cards Selection via OUT 1: b1: Expansion slot 1 (#02) b2: Expansion slot 2 (#04) b3: Expansion slot 3 (#08) b4: Expansion slot 4 (#10) | Slot 1, 2 and 3 reserved for 3 expansion cards Selection via OUT 1: b1, b2, b3 and b4 as for the original COMX b0: 0 select ROM banks, 1 select RAM banks b5-b7: select bank number |
| E000 - E7FF | Reserved for expansion ROM (replacing part of COMX BASIC ROM) | SB FW |
| E800 - EFFF | Reserved for expansion ROM | Expansion box ROM |
| F000 - F3FF | Not used | NVRAM & RTC |
| F400 - F7FF | Character Memory | Character Memory |
| F800 - FFFF | Page Memory | Page Memory (write) & SB FW (read) |

## Super Board EPROM Content

|  | SYSTEM ROM |  | EPROM 1 (SB Banks 0-3) | EPROM 2 (SB Banks 4-7) |
| --- | --- | --- | --- | --- |
| 0000-3FFF | SB BASIC ROM | 0000-1FFF | SB Main command handling | MON & SYSDISP |
|  |  | 2000-3FFF | Error handling, NVLIST & VER | TENNIS |
| 4000-47FF | SB FW E000-E7FF | 4000-5FFF | Help, printer commans & MEMDUMP | DMON, WORM, JOY, Q, MOVE, TV, PCNTL, PTV, HEX, BIN, GO40 GO80, BOOTMSG, LOGOTUNE, DWIDTH, DHEIGHT, POS, PKB, EF, LINE, SCREEN, JOYLOAD, NVPOKE, CLOCK, OLD, RTCFT, CARDB, CARDF |
| 4800-67FF | Not used |  |  |  |
|  |  | 6000-7FFF | DOS and Tape commands | SPACE & Graphic commands |
| 6800-6FFF | Expansion box ROM |  |  |  |
| 7000-77FF | Not used |  |  |  |
| 7800-7FFF | SB FW F800-FFFF |  |  |  |

# APPENDIX B – DETAILED MEMORY MAP

This document lists detailed memory locations for most SB FW routines as well as data locations.

The following color coding is used:

Black text: SB 1802 code

Green text: unused / spare memory

Blue text: data areas

Red text: info about code that is removed compared to the original COMX ROM

Orange text: Main routine description

Unchanged: info about original COMX ROM code

Note that not all code / locations are described!

## BASIC ROM (0000 - 3FFF)

| 0000 | - | 000C | RB = 0013, SEP B |
| --- | --- | --- | --- |
| 000D | - | 000F | Branch to 037D |
| 0010 | - | 0012 | Branch to 0258 |
| 0013 | - | 001E | Disable interrupts and set OUT 3 to F0 (normal pixel width, COLB12 = 11, Display off, No CFC, black BKG). |
| 0018 | - | 0246 | Start-up routine which is optimized and rewritten |
| 0018 | - | 001E | Set R2 to BDFF (instead of 4FFF which cause 4FFF RAM area to be destroyed at restarts) and change stack pointer to R2 |
| 001F | - | 0032 | Copy initial values from 0DA7-0DBE to 41C0-41D7 |
| 0033 | - | 004B | Initialize R7 and RF.0 to 0 Check on PAL/NTSC (EF2) and correct 41C3/41CA and set R7 to 8h and RF.0 to 80h for NTSC version. R7 is used for CDP1870 OUT 5 value and RF for the character of the COMX bars on the start-up screen. Values will be different for PAL/NTSC |
| 004C | - | 005A | Set RD=FFFF for pointer to PAGE RAM and clear PAGE RAM |
| 005B | - | 005D | Give Q pulse to start DMA RAM Refresh |
| 005E | - | 0071 | Fetch LOGOTUNE bit from NVRAM (bit 7 F3F0h), put it in bit 0 of RC and fill rest of RC with 3C40 which will start tune if bit 0 = 1 with the OUT 4 on 0070h. |
| 0072 | - | 0080 | Delay if LOGOTUNE is on |
| 0081 | - | 0088 | OUT 7 with F800 to define top of screen |
| 0089 | - | 00A2 | SHAPE COMX characters as defined from 0605-0A84. Note this routine uses R4=0C80 and R5=00AA followed by a SEP 4 to call the SHAPE routine at 0C80 and return with a SEP 5 to 00AD. |
| 00A3 | - | 00A9 | Entry: 00AA, print D on screen pointed in RD, INC D and return by branching to 00A3 which executes a SEP5. |
| 00AA | - | 00DE | PRINT COMX logo and bars on the screen |
| 00DF | - | 00F9 | Check location 4281/4282 (DEFUS value), if between 4400h and C400h and the low byte is 0Ch continue to add the ‘W = WARM START’ message on the screen, if not skip to 0108. |
| 00FA | - | 0104 | Check F0F3 bit 5 if ‘W = WARM START’ (boot message) should be printed |
| 0105 |  |  | Print boot message followed by remaining text as below. |
| 0108 | - | 0117 | Print remaining start-up text, loading R6.0 with 63 (R6.1 is already #FF) |
| 0118 | - | 0120 | OUT 3 with 40h(Double Pixel width, COLB10=01, Display on, No CFC, black BKG) OUT 5 with R7 (Double pixel height and 8/9 lines depending on PAL/NTSC mode) |
| 011E | - | 012C | Fetch LOGOTUNE bit from NVRAM (bit 7 F3F0h) and branch over logotone routine if switched off |
| 012D | - | 014D | Logotone routine |
| 014E | - | 0152 | Fetch GO80 bit from NVRAM (bit 6 F3F0) and branch over 80 column selection if switched off |
| 0153 | - | 0175 | GO80 selection routine Search for 80 column card by switching slots from 1 to 3. If not found continue regular boot on 019B If found skip over logo screen cycle routine by using a SEP 4 to 01C2 |
| 0176 | - | 017E | Force copyright screen during boot screen (C pressed) and continue on 01AC by using a SEP 5. This routine is called when ‘C’ is pressed via check on 0189 |
| 017F | - | 019A | Start routine in 0180. Wait routine including key press checks ‘C’ and ‘space’. Key C will branch to 0176 to force copyright screen, other keys (not ‘space or ‘C’) will exit routine to 01C2. Wait loop length is set to byte stored after ‘SEP 4’ call to 0180. |
| 019B | - | 01A1 | Set X to R5; R4=0180 |
| 01A2 | - | 01C1 | Logo screen cycle routine SEP 4, X calls the wait routine with a delay of ‘X’ After wait routine screen is changed by an OUT 3 to change COLB10 (color) or pixel width/height by an OUT 5. The OUT 5 used R7.0 to select NTSC or PAL mode. Delay on copyright screen is increased compared to original ROM |
| 01C2 | - | 01D0 | Clear screen (with ‘00’ instead of ‘20’ as in original ROM |
| 01D1 | - | 01EB | Get COLOR, CTONE and SCREEN info from NVRAM (F3E9, bit 0-3 and 5-6), use value with bit 7=1 (normal pixel width) with an OUT 3 to use colors in start-up. |
| 01EC | - | 01F1 | OUT 5 with R7 (normal pixel height and 8/9 lines depending on PAL/NTSC mode) |
| 01F2 | - | 0203 | Clear 4100-41AE |
| 0204 | - | 0209 | Set R1=0496 (start interrupt routine) |
| 020A | - | 021D | Set 4193 to 419B to default values, 419C to 41AE default set to 0 above |
| 021E | - | 0220 | Set OUT 1 to 0 to handle start-up of SB. |
| 0221 | - | 0226 | R3=0229 |
| 0227 | - | 0228 | Enable interrupt, X=R2 and P=R3 |
| 0229 | - | 0246 | Initialize register, R4=2E14, R5=31EB, R9=4370, RD=3302 |
|  |  |  | Continue on 0FFF |
| 0244 | - | 0257 | Spare |
| 02E4 | - | 02E6 | LBR FBF8, new scroll routine for proper clock clearing |
| 046C | - | 046F | LBR E6C7; NOP, call to updated print routine |
| 054E | - | 0561 | Updated interrupt branching to E025/E01F. Including a LDA 0 on 054E to handle a COMX without DMA. |
| 056E | - | 0570 | LBR 0DE0, part of updated interrupt routine clearing key press if ESC was pressed. |
| 0605 | - | 0A84 | COMX Standard character SHAPE definition |
| 0733 |  |  | Changed 08 to 00, to remove ‘red dot’ in shape for ‘!’ |
| 0741 | - | 0742 | Changed FE D4 to D4 FE to make shape ‘#’ more correct |
| 075B | - | 0662 | Moved 1 address up, to move shape ‘&’ on line up |
| 0A85 | - | 0AF7 | Optimized SHAPE command handling to allow routine to be used by USB SHAPE |
| 0BFC | - | 0C7F | COLOR routine |
| 0C5F |  |  | Changed LDI 63, PLO 9 to LDI 3F, PLO9. This value is used for the number of characters to be shaped in the 0C80 routine. The old routine shaped a max of 64 (40h) characters so even if 63h was loaded it would only change 40. The new optimize SHAPE routine shapes a max of 128 characters so using 63h causes too many characters to change color/shape. I changed the number to 3Fh as that excludes the ‘green’ 0. |
| 0C62 | - | 0C63 | Part of COLOR routine, changed sub routine call from 0C80 to FE5E, FE5E will call to 0C80 and after that set the last color shape mask back to NVRAM (b7/b6 on F3EA). |
| 0C80 | - | 0D0A | Optimized ‘SHAPE’ routine to include a check on USB FLASH setting (bit 7 NVRAM F3EB) |
| 0D0B | - | 0D34 | Part of TONE, MUSIC and NOISE routine, changed to skip sound setting if VOLUME is set 0. |
| 0D35 | - | 0D61 | Optimized VOLUME routine to include storing of VOLUME value in NVRAM (including parts on 22B2-) |
| 0D62 |  |  | Spare |
| 0D63 | - | 0D96 | CTONE Routine (unchanged) |
| 0D97 | - | 0DA1 | POP values from stack and restore RD, RC.0, RA.0 and R8.0. Used from CTONE and other routines |
| 0DA7 | - | 0DF4 | Removed POUT, TOUT routine and replaced with routines below. |
| 0DA7 | - | 0DBE | Initial values 41C0 to 41D7 |
| 0DBF | - | 0DCF | Spare |
| 0DD0 | - | 0DDF | NOT used as it will be overwritten by the FDC if connected |
| 0DE0 | - | 0DE8 | Part of updated interrupt routine, including a call to E01F and clearing of key press if ESC was pressed |
| 0DE9 |  | 0DF4 | Spare |
| 0E00 |  |  | PLOAD |
| 0E03 |  |  | DLOAD |
| 0E05 |  | 0E75 | PLOAD / DLOAD |
| 0F2B |  | 0F2D | Call to FEDD as part of new CPOS routine to check if DWIDTH is active |
| 0FFF | - | 1027 | Continuation of re-written start-up routine |
| 0FFF | - | 1005 | Set 42BB = R2.1, store high byte stack pointer on 42BB Set 42B7 = 0 |
| 1006 | - | 1007 | Call to 18D0, to set initial values for some system locations (key and character values) |
| 1008 | - | 100B | Call to E18A to: Call to 1AB5 (original code) to initialize default I/O routines on 428A-4291 Get USB VOLUME setting from NVRM Reset CNTL V/R and X buffers Set LINE/SCREEN editor Set PRINTER slot Set USB COLOR Set USB CHAR Auto boot 80 column CARD. |
| 100C | - | 100E | Call to FD39, call 1A6C (original code), set 80 column if applicable and shape line 10 to character number for all characters. |
| 100F | - | 1011 | Call to E215 to give 80 col WARM BOOT message if applicable. Give BASIC start-up message for 80/40 column modes; If needed do a call to FD39 for a DOS NEW |
| 1012 | - | 1016 | Call to E6B9 which will call DDFA in bank 0. DDFA will request initiation NVRAM if not done and then initiate NVRAM. Routine will return 0 if ‘WARM’ was selected and then skip the NEW routine below. |
| 1017 | - | 1027 | Initialize 4281/4282 to 440C (default BASIC DEFUS address), 4400 = 0 and call 1A47 (NEW) |
| 1028 | - | 106D | Main BASIC interpreter loop first clearing flags and printing READY prompt |
| 1028 | - | 1030 | Call 1451 to clear bit 0 to 6 in R8.1 and initialize 429E-42A6 Check flags bit 0 and 1 on 429D if either = 1 skip ‘READY’ prompt and continue on 104B. |
| 1031 | - | 1039 | Print READY prompt on screen |
| 103A | - | 1047 | Check if USB GRAPH is active (FEBE) then check if 80 column is active (E616) On return clear line after READY unless 80 column is active (if D != 0) |
| 1048 | - | 104A | Call E37F to print the ‘return’ after ‘READY’ and reset b8 of F3F7 (CLOCK) as no program is running. |
| 104B | - | 104D | Call to 18FC, command line input routine |
| 104E | - | 1050 | Call to 1E31, interpret command line |
| 1051 | - | 1056 | Check bit 0 of R8.1 if 1 (RUN mode) ‘return’ with a SEP 5 otherwise continue on 1057 |
| 1057 | - | 105C | Set RB = 42D0, which will store the interpreted BASIC command line |
| 105D | - | 1061 | Check bit 2 of R8.1 if 1 execute 1062 if 0 execute 106A |
| 1062 | - | 1069 | Call 1C00 Call 2E42 (LF + CR) Loop back to 1028 / start of main loop |
| 106A | - | 106E | Call 1CFA Loop back to 1028 / start of main loop |
| 106F | - | 10B5 | Error code handling |
| 107B | - | 107D | Call to FCAB to perform line feed including printer checks. |
| 1085 | - | 1087 | Call to E115 to print error code in text. |
| 10AE | - | 10B5 | Set stack pointer back to bottom (top) and return to main loop |
| 1227 | - | 122A | Replace POUT with CARD as in original expansion box |
| 124E | - | 132F | Command table shifted to replace TOUT with USB |
| 1330 | - | 1342 | Removed part of unused branching table |
| 1330 | - | 1342 | spare |
| 13C6 | - | 13DB | F&M Screen editor adaptation |
| 1406 | - | 142C | Default I/O Routine, output 1406, input 1409 |
| 1451 | - | 1474 | Clear bit 0 to 6 in R8.1 Copy content 1475-147D to 429E-42A6 |
| 1475 | - | 147D | Default values for address 429E-42A6 (44h, start user RAM and ‘empty call/return for BASIC functions |
| 1400 | - | 1402 | Changed start address ‘RUN’ to E36D to handle CLOCK off during run. |
| 1407 |  |  |  |
| 140A |  |  |  |
| 1414 | - | 142A |  |
| 1506 | - | 1507 |  |
| 14A0 | - | 14A9 | DEL |
| 14A0 | - | 14A4 | Print space (42AC) value on current cursor position |
| 14A5 | - | 14A9 | Print DEL (4280) value on current cursor position |
| 1530 | - | 1531 | Changed start address ‘PLOAD’ to FCD6 to do an INP 1 which will re-activate EF handling for tape. |
| 1542 | - | 1543 | Changed start address ‘DLOAD’ to FCDC to do an INP 1 which will re-activate EF handling for tape. |
| 1550 | - | 1551 | Changed start address ‘CALL’ to E373 to handle CLOCK off during CALL. |
| 1552 | - | 1553 | Changed start address VOLUME to 0D36 to allow a little more space to include storing of value in NVRAM |
| 1558 | - | 1559 | Changed start address ‘DOS’ to E010 which will call USB command routines which will check if a new SB DOS command is give. If not normal DOS routines will be called. |
| 155A | - | 155B | Changed start address ‘CARD’ to E817 as in original expansion ROM. |
| 1564 | - | 1565 | Changed start address ‘EDIT’ to E687 to handle incorrect arguments like (). |
| 1568 | - | 1569 | Changed start address ‘USB’ to F816 for command handling |
| 156A | - | 156B | Changed address 0DA7 to 0DA1, this is part of the TOUT and/or POUT routines and shouldn’t really be used anymore. To be safe I changed it to an address with SEP 5. |
| 15C0 | - | 15C1 | Changed start address ‘USR’ to E379 to handle CLOCK off during USR. |
| 17C9 | - | 17CC | Part of LIST code, intercepting if a USB command is detected. If so a call is made to E3CF to handle proper formatting of USB commands. |
| 17F2 | - | 17F4 | F&M Screen editor adaptation (part of EDIT code) |
| 1840 | - | 1844 | Part of EDIT code, calling FB6C to handle different EDIT behavior in screen editor. |
| 18D0 | - | 18F8 | Initialize: 4280 = 86, DEL key value 42AA = 8C, CNTL R key value 42AB = 8D, CNTL C key value 42AC = 20, spacebar key value 42AD = 85, clear to end of screen output value 42AE = 87, CNTL S key value 42B5 = 44 = ‘,’ 42B6 = 49 = ‘1’ 42CE = 43 = ‘+’ 42CF = 8D, CNTL C key value (used in EDIT, and 19AEh) |
| 18F9 | - | 18FB | Call 2E42 to give a LF+CR before continuing command line input routine on 18FC |
| 18FC | - | 1988 | Command line input routine R8.1 bit 0 1: program is running 0: command line mode |
| 18FC | - | 190A | RC.0 = R8.1 bit 0 (1 = RUN MODE, 0 = Command line) RC.1 = bit 1 and 0 from 429D If 429D bit 1 or 0 are 1 skip ‘:’ or ‘?’ If R8.1 = 0 branch to E10B to check status USB SCREEN and print ‘:’ if not active and return to 1910. If USB SCREEN is active return to 1913 |
| 190B | - | 190D | If R8.1 = 1 branch to E180 to print ‘?’ followed by a ‘0’ character, return to 1910 |
| 1910 | - | 1912 | Call 2CD3 to print character in D to current screen position (: or ‘0’) |
| 1913 | - | 191C | Set R7 to command line buffer 4200, call ‘In hook’ on 428A and store resulting key input to stack (M(R2)). |
| 191D | - | 1922 | If RUN mode (RC.0 != 0) or if command line buffer is not empty (R7.0 != 0) branch to 192D. For USB SCREEN mode R7.0 will always be != 0 as it is pointing to the 42D0 interpreted line buffer, possibly not fully optimized |
| 1923 | - | 1928 | Check if input is ‘CR’ (0Dh) if so loop back to 18F9 for a LF+CR and new input |
| 1929 | - | 192C | Check if input is ‘space’ if so loop back to 1913 for reset to start of command line buffer and new input |
| 192D | - | 1932 | Check if input is ‘CNTL C’ (42DA) if so loop back to 18F9 for a LF+CR and new input |
| 1933 | - | 1937 | Check if input is ‘CNTL R’ (42AA) if not continue on 1952 |
| 1938 | - | 1951 | CNTL R (USB LINE) Copy 4000-405F (CNTL R buffer) to 4200-405F (command line buffer) and screen via the out-hook (428E). The buffer is copied until 0dh is found or 405F is reached. |
| 1952 | - | 1956 | Check if input is ‘DEL’ (4280) if not continue on 1961 |
| 1957 | - | 1960 | DEL pressed If R7.0 = 0 (empty line buffer) do nothing and return to 18FC for ne input. Otherwise call 14A0 to handle ‘DEL’ and then wait for new input by branching to 1919. |
| 1961 | - | 196D | Store input (stack value) on command line buffer M(R7) and CNTR buffer and increct command line buffer pointer with 1 (R7+1) |
| 196C | - | 1971 | If CR was not pressed continue on 197C |
| 1972 | - | 197B | CR pressed Set TAB value to 0 (429B), end routine on 1988 if RC.1 != 0 (429D bit 0/1). Otherwise print a LF (0Ah). |
| 197C | - | 1987 | Check for command line buffer full (R7.0 = 60) if not continue waiting for next input at 1919 otherwise print ‘DEL’ character on screen via outhook 428E and continue on 195B to handle ‘DEL’ |
| 1988 |  |  | SEP 5 to end command line input routine |
| 1A47 | - | 1A7F | NEW |
| 1A6C | - | 1A7F | CLS, initialize 429D (flags), 429C, 42B3 to 0, 42BC to 41h, 42BA to 7Ah and 42B9 to B1. |
| 1AB5 | - | 1ACE | Initialize 428A – 4291, copied from 1ACF-1AD6 (call to input/output routines) |
| 1ACF | - | 1AD6 | Call to default input (1409) and output (1406) routines |
| 1B9E | - | 1BA0 | Part of LET routine, calling E33E where a check is done on both CARD and USB statements to allow A=USB commands |
| 1D01 | - | 1D02 | Changed to FB66, to call subroutine to check if a line number >= FFFF has been given. Bug fix of original COMX BASIC. |
| 1DFA | - | 1E30 | Spare |
| 1E31 | - | 1EDC | Interpret command line |
| 221C | - | 22D8 | Old RENUMBER location, RENUMBER moved to SB bank 7. |
| 221C | - | 22B1 | USB CPEEK |
| 22B2 | - | 22C8 | Store VOLUME value on RA (41C9) and NVRAM |
| 22C9 | - | 22D8 | Spare |
| 241A | - | 241D | LBR E328, NOP. String assignment handling, allowing A$=USB commands. |
| 2600 | - | 2602 | LBR E35D, part of IF handling to allow USB commands to be used in IF statements. |
| 26C8 | - | 26F8 | INPUT |
| 26C8 | - | 26D0 | Check is BASIC is in RUN mode (R8.1 bit 0 = 1) if not give ERROR 11h |
| 26D1 | - | 26D8 | If an open quote (CFh) is detected on BASIC line (M(RB)) call 2E35 to print all text specified on line until a close quote is detected (CEh) |
| 26D9 | - | 26DD | Fetch low byte of current interpreted command line buffer from 4287 and high byte from Rf.1 store as one pointer in RE (42D0 range) |
| 26DE | - | 26E6 | Check if INPUT is requesting input to a string variable (M(RB) = D7h) if so branch to input string routine on 2E49. |
| 26E7 | - | 26EA | Call to E2B0 to handle input of the integers (104B) and handle empty lines as well as error message for string. On return the correct low byte of the interpreted command line is in D and stored in RE.0. |
| 26EB | - | 26ED | Store the integer on the interpreted command line in the correct variable (call to 3000) |
| 26EE | - | 26F1 | Check if more variables are specified on BASIC line (comma / C2h found), if so loop back to 26E7 |
| 26F4 | - | 26F8 | Store current low byte of interpreted command line (42D0) on 4287, command end. |
| 26F9 | - | 26FF | Spare |
| 280D | - | 280F | LBR E34D, part of PRINT routines, to allow USB commands to print return values. |
| 2A05 |  | 2A07 | LBR FD91, string assignment handling, allowing A$=USB commands. |
| 2AEE |  |  | Changed 3A to 30 (BNZ to a BR) |
| 2CD3 | - | 2CFF | Print D on current screen position |
| 2D7B |  |  | Changed 3A to 30 (BNZ to a BR) |
| 2E35 | - | 2E41 | Print data starting on M(RB) on current screen position until a close quote (CEh) is detected |
| 2E42 | - | 2E48 | Print LF + CR |
| 2E49 |  |  | INPUT string |
| 3000 |  |  | Store the integer on the interpreted command line in the correct variable |
| 321E | - | 3225 | CLS, one NOP removed on 3225 |
| 3226 | - | 322A | Spare |
| 322B | - | 3222 | Print characters after SEP 4 call to current screen position until ‘0’ |
| 3D0B | - | 3D0C | LBR FAA9. To handle bug in READ feature which crashed if no DATA statements are available. |

## RAM (4000 - BFFF)

| 4000 | - | 405F | CTRL R Buffer |
| --- | --- | --- | --- |
| 4100 | - | 41xx | Scratch area? |
| 4193 | - | 4194 | Cursor position within @F800-@FFFF location, default F800h |
| 4195 | - | 4196 | Top left screen position within @F800-@FFFF location, changes after scrolling, default F800h |
| 4197 | - | 4198 | Cursor position, assuming top left corner = 0, default 0 |
| 4199 |  |  | ? default FFh |
| 419A |  |  | Column counter, default 0 |
| 419B |  |  | Cursor on/off (off = 0), default FFh |
| 419D |  |  | Timer on/off (off = 0) |
| 419E | - | 41A0 | 24 bits timer value, count back to 0 if @419D != 0 |
| 41A1 | - | 41A2 | Start address timer, a jump is needed to @054E at the end of timer routine. Usable registers: B, A and E, register 1 is program counter. |
| 41A3 |  |  | Raw keyboard value, changed after changing value to 0 |
| 41A4 |  |  | Direct keyboard value |
| 41A5 |  |  | Counter for key repeat |
| 41A6 | - | 41A7 | Start address ESC routine |
| 41A8 |  |  | If ESC is pressed equals to #FF |
| 41AE | - | 41B3 | Printer Settings and info |
| 41B4 | - | 41BF | Spare? |
| 41C0 |  |  | Last value OUT 3 |
| 41C1 |  |  | Low byte of last OUT 4 |
| 41C2 |  |  | High byte of last OUT 4 |
| 41C3 |  |  | Low byte of last OUT 5 |
| 41C4 |  |  | High byte of last OUT 5 |
| 41CC | - | 41CF | Call to MUSIC routine |
| 41D0 | - | 41D3 | Call to TONE routine |
| 41D4 | - | 41D7 | Call to NOISE routine |
| 41D8 | - | 41E0 | Spare |
| 4280 |  |  | DEL key value, 86h |
| 4281 | - | 4282 | DEFUS value |
| 4283 | - | 4284 | EOP (End Of Program) value |
| 4287 |  |  | Low byte of current position on 42D0 interpreted command line |
| 428A | - | 428D | In hook, call to input routine |
| 428E | - | 4291 | Out hook, call to output routine |
| 4292 | - | 4293 | End array/start string value |
| 4294 | - | 4295 | Start array value |
| 4296 | - | 4297 | Line number TIMOUT |
| 4299 | - | 429A | EOD (End Of Data) and end string value |
| 429B |  |  | X value TAB |
| 429C |  |  | ? default 0 |
| 429D |  |  | Flags, default 0 Bit 0: if 1 no READY prompt should be given Bit 1: if 1 no LF should be done |
| 429E |  |  | Start address user RAM, default 44h |
| 429F | - | 42A2 | Call to BASIC functions |
| 42A0 |  |  | Used by COMX BASIC for start address of latest used command. FW uses this in certain cases to detect what type of command is being used. For example to differentiate between PRINT USB Q and A=USB Q |
| 42A1 |  |  | Used during command handling to ‘save’ R8.1. |
| 42A3 | - | 42A6 | Subroutine call to the requested USB or DOS command. The same locations are also used by COMX BASIC for some command handling subroutine calls |
| 42A8 |  |  | Used by the F&M Screen Editor, 0 line editor, 1 screen editor, 2 USB BROSWER editor |
| 42A9 |  |  | RE.1 at call of 1AB5 routine (initialize normal I/O calls), used in CALL/USR to restore to RE.1 before calling user routine. Don’t understand the purpose. |
| 42AA |  |  | CNTR R key value, 8Ch |
| 42AB |  |  | CNTR C key value, 8Dh |
| 42AC |  |  | Spacebar key value, 20h |
| 42AD |  |  | Clear to end of screen output value, 85h for 40 column and 0Dh for 80 column mode |
| 42AE |  |  | CNTL S key value, 87h |
| 42B1 | - | 42B2 | DATA pointer |
| 42B3 |  |  | ?, default 0 |
| 42B5 |  |  | ‘,’, 44h |
| 42B6 |  |  | ‘1’, 49h |
| 42B7 |  |  | ?, default set to 0 |
| 42B9 |  |  | ?, default B1h |
| 42BA |  |  | ?, default 7Ah |
| 42BB |  |  | High byte value of R2 / Stack pointer, normal start value BDh |
| 42BC |  |  | ?, default 41h |
| 42CE |  |  | ‘+’, 43h |
| 42CF |  |  | CNTL C key value (used in EDIT and 19AEh), 8Dh |
| 42D0 | - | ? | Interpreted BASIC command line |
| 4300 | - | 4368 | Storage A, B, C.... Z, 4 bytes per variable |
| 4370 | - | ? | Command parameter buffer |
| 43F9 |  |  | Used by the F&M Screen Editor for the last character on the cursor position |
| 43F9 | - | 43FF | USB TDSAVE / TDSAVE+ buffer |
| 43FD | - | 43FF | USB DATE buffer |
| 4400 | - | Stack | User RAM |
| BDFF |  |  | ‘Start’ of stack |
| BE80 | - | BEFF | DOS buffer but also used by USB commands for the USB PC <-> COMX buffer. Also used by some USB commands (WORM, TENNIS, SPACE, MON, DMON) for storing temporary data. |
| BF42 |  |  | Current OUT 1 value (selected slot/bank) |
| BFFB |  |  | USB PLOT Character number pointer (to DF80-DFFF) |
| BFFC |  |  | Graphic Screen + 1 (0 = off) |
| BFFD |  |  | Printer slot if connected |
| BFFE |  |  | OUT 1 value (selected band/slot) at USB/DOS command entry |
| BFFF |  |  | Last specified USB CHAR |

## SB ROM Bank 0 (C000 - DFFF)

| C000 |  |  | 0, indicating ROM |
| --- | --- | --- | --- |
| C001 |  |  | 21, indicating SB FW ROM bank 0 |
| C002 |  |  | 10, indicating bank 0 slot code 10 |
| C003 | - | C00F | Identification text: SBV1.2 - MAIN |
| C010 | - | C012 | LBR C915, USB command handling routine called is ROM is switched in via a CARD command |
| C013 | - | C3F5 | USB command table: Command text, end is indicated by a code with b6 and b7 = 0 Instead of text also a command code could be used (identified by >80) i.e. SCREEN = A4. Type code: b0 = 0 command always returns a value (STR/INT) b1 = 1, command can return STR / INT b2 = 1, command will exit ‘USB command’ routine and branch back to BASIC b3 = DOS command b4 = 1, command will switch printer off b5 = not used b6/b7 = 0 (used as end code for command text) Start address (2 bytes) Slot code (if != 0) Second type (if != 0, used when different types are needed for one command. Example: USB Q and INT = USB Q. Second start address (2 bytes, if second type was detected) Second slot code (if != 0) End command code = 0 Note for commands including sub text of other commands the shortest command should come latest in the table. i.e. TIME should come after TIMEAM. |
| C417 | - | … | USB PSAVE |
| C53A | - | … | USB PLOAD |
| C8C1 | - | … | USB DSAVE |
| C9E3 | - | … | USB CD |
| CA1B | - | … | USB MKDIR |
| CA34 | - | … | USB CAT |
| CC45 | - | … | USB RMDIR |
| CC77 | - | … | USB DEL |
| CD77 | - | … | USB RTCPC |
| CDBA | - | … | USB SYSDEF |
| CE12 | - | … | USB DATE |
| CFFD | - | … | USB TIME |
| D0B8 | - | … | USB TIMEPM |
| D0D0 | - | … | USB TIMEAM |
| D163 | - | ... | USB NVSAVE |
| D17E | - | … | USB SYSSAVE |
| D199 | - | … | USB NVLOAD |
| D201 | - | … | USB SYSLOAD |
| D26E | - | ... | USB INP |
| D2CF | - | … | USB OUT |
| D35F | - | ... | USB HISTORY |
| D3CB | - | ... | USB NVPUT |
| D533 | - | ... | USB NVGET |
| D595 | - | ... | USB NVIGET |
| D62F | - | ... | USB NVSTART |
| D5F4 | - | ... | USB NVSGET |
| D730 | - | ... | USB NVCLR |
| D766 | - | ... | USB NVDEL |
| D78B | - | ... | USB NVLIST: startup, continue in bank 1 on DAED |
| D7D6 | - | ... | USB RSAVE |
| D818 | - | … | USB RLOAD |
| D888 | - | ... | USB MOVE |
| D8F0 | - | ... | USB IMGTODISK |
| D98F | - | ... | USB IMGTODISK |
| D9F9 | - | ... | USB IMGTEST |
| DA13 | - | … | USB JOY |
| DA1E | - | … | INT = USB Q |
| DA2D | - | … | USB EF |
| DA38 | - | ... | USB POS |
| DA43 | - | … | USB DLOAD |
| DAEF | - | ... | USB BSAVE |
| DB7E | - | ... | USB BLOAD |
| DC57 | - | ... | USB COMP |
| DD51 | - | DD57 | Check online mode if off return 0 |
| DD58 | - | ... | USB HSWEB |
| DD84 | - | ... | USB URL |
| DDA6 | - | ... | USB URLGET |
| DE25 | - | DE47 | USB BROWSER |
| DE48 | - | DEC6 | If NVRAM is not initiated, request initiation and then initiate NVRAM. Initiate NEW unless WARM start was selected. NEW jump to 102D otherwise 103E |
| DEC7 | - | ... | URL DISP |
| DE9D | - |  | USB BROWSER: URL ‘input’ save routine |
| DEEF | - | … | USB EMAIL |
| DF09 | - | DFB7 | Some text |
| DF81 | - | DFDF | Spare |
| DFE0 | - | DFE3 | Text: ‘ AM’ |
| DFE4 | - | DFE8 | Date/time mapping table |
| DFE9 | - | DFEC | Text: ‘ PM’ |
| DFED | - | DFEF | RTC mapping |
| DFF0 | - | DFF3 | Date/time mapping table |
| DFF4 | - | DFFF | Number of days per month (DFF4 = Jan, DFFF = Dec) |

## SB ROM Bank 1 (C000 - DFFF)

| C000 |  |  | 0, indicating ROM |
| --- | --- | --- | --- |
| C001 |  |  | 22, indicating SB FW ROM |
| C002 |  |  | 30, indicating bank 1 slot code 30 |
| C003 | - | C00F | Identification text: SBV1.2 - ERR |
| C010 | - | C012 | LBR F800, USB command handling routine called is ROM is switched in via a CARD command |
| C013 | - | C13B | Text error routines |
| C10B | - | C125 | Find and print error text Input: RA.0 = error code |
| C126 | - | C13B | Find error text and store in BE80 buffer Input: RA.0 = error code |
| C13C | - | C15C | Call subroutine in other bank Input: M[P+1]=slot M[P+2/3]=address |
| C15D | - | D792 | Error text |
| D818 | - | D8BF | Spare |
| D8C0 | - | D95B | Game/program names, used in USB NVLIST |
| D95C | - | D969 | Store new CHAR value in NVRAM Input: D=new CHAR |
| D96A | - | D98C | Fetch command arguments |
| D98D | - | DA7F | USB CHAR |
| DADB | - | DCC4 | Continue USB NVLIST (main code) |
| DD08 | - | DD7A | USB VER |
| DDC5 | - | DE05 | Get USB COLOR mask and set as last COLOR mask in NVRAM. Get USB CHAR from NVRAM and call CHAR. (DDEF) Get 80 column auto boot from NVRAM is set call E203 |
| DE14 | - | DE3D | USB BROWSER re-shape routine |
| DE3E | - | DE6C | Switch off USB GRAPH (called if at ‘READY’ prompt) no USB GRAPH (0) was done. |
| DE6D | - | DF12 | spare |
| DF13 | - | DFFC | Lower case shapes |
| DFFD | - | DFFF | FW Version date: DD - MM - YY |

## SB ROM Bank 2 (C000 - DFFF)

| C000 |  |  | 0, indicating ROM |
| --- | --- | --- | --- |
| C001 |  |  | 22, indicating SB FW ROM |
| C002 |  |  | 50, indicating bank 2 slot code 50 |
| C003 | - | C00F | Identification text: SBV1.2 - HELP |
| C010 | - | C012 | LBR F800, USB command handling routine called is ROM is switched in via a CARD command |
| C013 | - | .. | HELP print routines |
| C216 | - | D95D | HELP text per command |
| D95E | - | DB40 | spare |
| DB41 | - | DCA2 | HELP text for HELP command |
| DCA3 | - | DCCB | Shape cursor to original |
| DD4B | - | .. | USB PLIST |
| DD7D | - | .. | USB PPR / USB PPRINT |
| DD97 | - | .. | USB PTEST |
| DDD3 | - | .. | USB PMEMDUMP |
| DDEE | - | .. | USB PON |
| DE26 |  | .. | USB POFF |
| DE57 | - | .. | USB PSET |
| DF7C | - | .. | USB HELP |
| DfC1 | - | DFDD | Shape cursor to original and save R8, RC and RE on stack |
| DFDD |  | DFF5 | spare |
| DFF6 |  | DFFF | Original cursor shape |

## SB ROM Bank 3 (C000 - DFFF)

| C000 |  |  | 0, indicating ROM |
| --- | --- | --- | --- |
| C001 |  |  | 22, indicating SB FW ROM |
| C002 |  |  | 70, indicating bank 3 slot code 70 |
| C003 | - | C00F | Identification text: SBV1.2 - DISK |
| C010 | - | C012 | LBR F800, USB command handling routine called is ROM is switched in via a CARD command |
| C013 | - | .. | DOS BOOT |
| C0E0 | - | .. | DOS LOCK |
| C260 | - | .. | DOS UNLOCK |
| CEA1 | - | .. | DOS INIT |
| CEF5 | - | .. | DOS STARTUP |
| CF2B | - | .. | DOS LABEL |
| D031 | - | .. | DOS DISKCOPY |
| D0B7 | - | .. | DOS FILECOPY |
| D100 |  | D129 | Copy USB BROWSER text (DE32-DE67) to RAM for use in browser |
| D12A |  | D19A | Checkbox and radio routine (USB BROWSER) |
| D19B |  | D219 | 7F (127 decimal) bytes spare |
| D21A |  | D6F6 | Part of COPY code, will be copied to AF00 on DOS DISKCOPY |
| D6F7 |  | D743 | Part of COPY code, will be copied to B400 on DOS DISKCOPY |
| D744 |  | D834 | Part of INIT code, will be copied to B400 on DOS INIT and DOS STARTUP |
| D834 |  | D8A8 | Part of INIT code, will be copied to B300 on DOS INIT and DOS STARTUP |
| D8A9 |  | DAFF | Part of INIT code, will be copied to B000 on DOS INIT and DOS STARTUP |
| DB00 |  | DEFF | BOOT code will be copied to B700 on DOS BOOT |
| DE32 |  | DE7F | Text: ‘gO TO url:’, ‘lOADING PAGE…’ and ‘sENDING EMAIL’ including spacing and reversed to allow for USB CHAR(3) use in USB BROWSER |
| DE80 |  | DE9F | 20 (32 decimal) bytes spare |
| DEA0 |  | .. | USB TSAVE and TSAVE+ |
| DEA3 | - | .. | USB TDSAVE and TDSAVE+ |
| DEA6 | - | .. | USB TLOAD and TLOAD+ |
| DEA9 | - | .. | USB TDLOAD and TDLOAD+ |
| DF00 | - | DF80 | Part of INIT code, will be copied to B4F0 on DOS INIT |
| DF81 | - | DFFF | Part of STARTUP code, will be copied to B4F0 on DOS STARTUP |

## SB ROM Bank 4 (C000 - DFFF)

| C000 |  |  | 0, indicating ROM |
| --- | --- | --- | --- |
| C001 |  |  | 22, indicating SB FW ROM |
| C002 |  |  | 90, indicating bank 4 slot code 90 |
| C003 | - | C00F | Identification text: SBV1.2 - MON |
| C010 | - | C012 | LBR F800, USB command handling routine called is ROM is switched in via a CARD command |
| C013 | - | C028 | MON: text ‘PROTECTED and ‘UNPROTECTED’ |
| C029 | - | C034 | MON: text ‘HEX.’ and ‘TEXT’ |
| C035 | - | C057 | Find printer CARD, if found store slot code on BFFD |
| C058 | - | C095 | Print number routine 1 |
| C05D | - | C095 | Print number routine 2 |
| C096 | - | C245 | MON: screen ‘READ REGISTERS’ |
| C246 | - | C300 | MON: screen ‘AUTO STORE’ |
| C300 | - | C44A | MON: screen ‘CHANGE’ 2nd screen |
| C44A | - | C4E2 | MON: screen ‘DUMP’ |
| C4E3 | - | C4EB | MON: text ‘↑DELETE’ |
| C4EC | - | C51D | MON: table for address positions ‘CHANGE’ |
| C51E | - | C526 | MON: text ‘↑INSERT’ |
| C527 | - | C531 | MON: text ‘WHITE’ and ‘BLUE’ |
| C532 | - | C612 | MON: screen ‘MOVE’ |
| C613 | - | C6E7 | MON: screen ‘CHANGE’ 1st screen |
| C6E8 | - | D80B | Continue USB MON (main code) |
| D80C | - | D823 | Part of SYSDISP printing off or on |
| D824 | - | DC31 | USB SYSDISP |
| DC44 | - | DC4C | Print to screen routine via DC3B Print all characters M[R6] and increase R6 until ‘0’ is found |
| DC4D | - | DC9D | Print routine checking USB CHAR setting, so depending on setting lower case will or will not be used. |
| DC9F | - | DCBD | Part of USB SYSDISP, routine will switch to printer card and check if a serial or parallel card is connected. |
| DCBE | - | DCE2 | Part of USB SYSDISP |
| DCE3 | - | DD05 | Check if NVRAM is writable / available, if not give error message 5B or 61 |
| DD06 | - | DD3A | Check if printer is active, if active select printer, branch to M[R6+1/R6+2] and switch back to slot on M[R6]. If no printer active just branch to M[R6+1/R6+2]. |
| DD54 | - | DD60 |  |
| DD3B | - | DD53 | Error code routine |
| DD61 | - | DD6D | Part of USB SYSDISP, printing ‘Printer’ |
| DD6E | - | DE13 | USB BROWSER passwd input routine |
| DE13 | - | DE57 | spare |
| DE58 | - | DEEF | USBBROWSER passwd input return jump table |
| DE60 | - | DFFF | MON: startup screen |

## SB ROM Bank 5 (C000 - DFFF)

| C000 |  |  | 0, indicating ROM |
| --- | --- | --- | --- |
| C001 |  |  | 22, indicating SB FW ROM |
| C002 |  |  | B0, indicating bank 5 slot code B0 |
| C003 | - | C00F | Identification text: SBV1.2 - TENN |
| C010 | - | C012 | LBR F800, USB command handling routine called is ROM is switched in via a CARD command |
| C013 | - | C20E | TENNIS: Start-up code |
| C20F | - | C6DA | BROWSER: Main code |
| C6DB | - | C670C | 32 (50 decimal) bytes spare |
| C70D | - | C7BB | TENNIS: Screen A / B |
| C7BC | - | C7CB | TENNIS: GAME OVER text |
| C7CC | - | C8FE | TENNIS: Screen C / D |
| C8FF | - | CA1D | TENNIS: Screen E / F |
| CA1E | - | CAB4 | TENNIS: Shapes |
| CAB5 | - | CADD | TENNIS: Screen G / H |
| CADE | - | CD81 | TENNIS: Game tables (byte 1: ?, 2: game number, 3: game letter, 4+5: high score location, 6+7: screen map location) |
| CD82 | - | CE9F | TENNIS: Screen I / J |
| CEA0 | - | CFFF | TENNIS: Screen K / L |
| D000 |  | DE46 | TENNIS: Code main part |
| DE47 | - | DE48 | 2 bytes spare |
| DE49 |  | DFAC | TENNIS: HELP text |
| DFB8 | - | DFD7 | TENNIS: Some table |
| DFD8 | - | DFFF | TENNIS: row 24 text |

## SB ROM Bank 6 (C000 - DFFF)

| C000 |  |  | 0, indicating ROM |
| --- | --- | --- | --- |
| C001 |  |  | 22, indicating SB FW ROM |
| C002 |  |  | D0, indicating bank 6 slot code D0 |
| C003 | - | C00F | Identification text: SBV1.2 - DMON |
| C010 | - | C012 | LBR F800, USB command handling routine called is ROM is switched in via a CARD command |
| C013 | - | C015 | WORM: Interrupt routine |
| C016 | - | C023 | DMON: WHITE / BLUE text |
| C024 | - | C04B | DMON: Shapes |
| C04C | - | C069 | WORM: Shapes |
| C06A | - | C099 | DMON: Screen locations ‘change’ |
| C09A | - | C179 | DMON: Start screen |
| C17A | - | C188 | DMON: Error text |
| C188 | - | C18C | DMON: 15 spaces |
| C18C | - | C26E | DMON: Change screen |
| C26E | - | C2DE | DMON: Dump screen |
| C2Df | - | C309 | DMON: shape routine |
| C30A | - | C324 | Print routine, print value on m[R8] and increase R8. If R8 = 0, take next byte as character and following as the number and repeat that character ‘number’ times. End by 2 zeros. |
| C544 | - | .. | DMON: main code |
| C9AE | - | CA1B | DMON: startup code, initiate memory etc. |
| CA40 | - | .. | USB CTONE |
| CA48 | - | .. | USB COLOR |
| CA6B | - | CA8D | Spare |
| CABB | - | .. | USB CLOCK |
| CB03 | - | .. | WORM: main code |
| D1B9 | - | D1D9 | Call subroutine in other bank Input: M[P+1]=slot M[P+2/3]=address |
| D1DA | - | D1F1 | WORM: switch interrupt off, store high score etc |
| D1F2 | - | D1FE | WORM: sound routine |
| D1FF | - | D227 | Sound off routine |
| D228 | - | .. | USB RTCFT |
| D253 |  | .. | USB OLD |
| D2E0 |  | .. | USB LINE |
| D312 |  | .. | USB SCREEN |
| D34F |  | .. | USB NVPOKE |
| D529 |  | D539 | Get (x) from command line and return x in D |
| D53A |  | .. | USB TV |
| D55D |  | .. | USB Q |
| D567 |  | .. | USB DMON: start code like CHAR and CLS routines |
| D6F2 |  | .. | USB WORM: start code like CHAR and CLS routines |
| D75A |  | D786 | USB SPACE: start code like CHAR and CLS routines |
| D79C |  | D7B9 | USB GRAPH |
| D7BA |  | D7BE | spare |
| D87B | - | .. | USB PCNTL |
| D8DB | - | .. | USB DWIDTH |
| D8F7 | - | .. | USB DHEIGHT |
| D917 | - | .. | USB TENNIS: start code like CHAR and CLS routines |
| D939 |  |  | USB POS |
| D9D1 | - | .. | USB MON: start code like CHAR and CLS routines |
| D9F0 | - | .. | USB LOGOTUNE |
| DA0A | - | .. | USB GO (40, 80 and 80(x)) |
| DA60 | - | .. | USB BOOTMSG |
| DA97 | - | .. | USB PTV |
| DAC6 | - | .. | USB PKB |
| DAE3 | - | .. | USB HEX |
| DB38 | - | .. | USB BIN |
| DB7B | - | .. | Continue LET CARD command check |
| DBB3 | - | .. | LET CARD F routine |
| DBF7 | - | .. | USB ONLINE |
| DC83 | - | .. | USB CLS |
| DCDF | - | DDB1 | USB MEMDUMP |
| DDB2 | - | DDE7 | Shape routine for USB BROWSER |
| DDE8 | - | DDF7 | USB BROWSER: CLS + Shape (was C650) |
| DDF8 | - | DE16 | USB BROWSER: Shape standard char set (was C510) |
| DE17 | - | DE56 | USB BROWSER: input CR routine |
| DE57 | - | DE6C | Check on end of command |
| DE6D | - | DE85 | spare |
| DE86 | - | DF09 | USB BROWSER: Shapes |
| DF0A | - | DF17 | WORM: text ‘C R A S H !!’ |
| DF18 | - | DF3B | WORM: text first line |
| DF40 | - | DFFF | WORM: table |

## SB ROM Bank 7 (C000 - DFFF)

| C000 |  |  | 0, indicating ROM |
| --- | --- | --- | --- |
| C001 |  |  | 22, indicating SB FW ROM |
| C002 |  |  | F0, indicating bank 7 slot code F0 |
| C003 | - | C00F | Identification text: SBV1.2 – SPAC |
| C010 | - | C012 | LBR F800, USB command handling routine called is ROM is switched in via a CARD command |
| C013 | - | C01A | SPACE: Jump table |
| C01B | - | C022 | SPACE: Data address table |
| C023 | - | C037 | SPACE: table |
| C038 | - | C03F | SPACE: data |
| C040 | - | C0A6 | SPACE: data |
| C0A7 | - | C0C0 | Copy data to RAM bank routine |
| C0C1 | - | C0E2 | SPACE: data |
| C0E3 | - | C104 | SPACE: data |
| C105 | - | C133 | SPACE: data |
| C134 | - | C157 | SPACE: data |
| C158 | - | C17A | SPACE: data |
| C17B | - | C1A7 | SPACE: data |
| C1A8 | - | C1CD | SPACE: first screen row |
| C1CE | - | C277 | SPACE: shapes |
| C278 | - | D28F | SPACE: code |
| D290 | - | D316 | SPACE: code, initiation and high score routines |
| D317 |  | D337 | Call subroutine in other bank (start-up; calling common routine at FC51) |
| D338 | - | D355 | SPACE: high score handling and call to HSWEB |
| D356 | - | DE34 | SPACE: return to BASIC (B key) |
| D388 | - | D3A0 | SPACE: all sound off |
| D3A1 | - | D3B9 | SPACE: Sound on/off (S key) |
| D3BA | - | D3C4 | SPACE: sound |
| D3C5 | - | D4E6 | USB BROWSER input routine |
| D52B | - | D5EF | USB GRAPH (continued, jump in from bank 6 D7B7 |
| D5D2 | - | D649 | USB PLOT (X, Y, color, char) USB PLOT (X, Y, color) Command handling resulting in: R8.0 = X RA.0 = Y R7.1 = Shape color bits (7/6), character color bit (0) R8.1 = character number |
| D64A | - | D737 | PLOT (X, Y, color) On input: R8.0 = X RA.0 = Y R7.1 = Shape color bits (7/6), character color bit (0) RB = DF4x screen info pointer Destroys content of R9, RC, RF Code: Set RC = Cxxxx (screen location in bank 7 based on X, Y and RB) Check if X / Y are in screen range if not exit RD, R8.0, RA.0 SAVED on Stack RD = F808 / F80F to store and read from RAM bank 7 Calculate RC to specify character covering X, Y-> rest values stored in R8.0/R8.1 If char height != 10 read current character from char memory (D4 EF55 uses R9 as screen position by adding 3800 to RC) otherwise read from RAM bank 7 with SEP D. If current char = 0 get next char from R9 (BFFB) pointer to DF80 area Re-shape character to space (only for height != 10) using R9 and RF Store character on screen (height !=10) or in RAM bank 7 with SEP D Add 3800 to RC so it can be used as screen pointer Store character and color bit on RC and R9 (i.e. print char on screen and on shape pointer) Shape correct line via rest values of X/Y R8.0/R8.1 using RD and RF and pixel color from R7.1 |
| D738 | - | D7BE | PLOT (X, Y, color, char) |
| D7BF | - | D820 | LINE OCTANT 1 |
| D821 | - | D881 | LINE OCTANT 0 |
| D882 | - | D8B3 | LINE (X, Y, color, X2, Y2) |
| D8B4 | - | D8CD | USB LINE(X, Y, color, X2, Y2) Command handling R8.0 = X RA.0 = Y R7.1 = Shape color bits (7/6), character color bit (0) R8.1 = X2 RA.1 = Y2 |
| D8CE | - | D8DD | USB CIRCLE(X, Y, color, radius) Command handling |
| D8DE | - | D99A | CIRCLE(X, Y, color, radius) |
| D99B | - | D9AA | USB ELLIPSE (X, Y, color, A, B) |
| D9AB | - | DA87 | ELLIPSE(X,Y, color, A, B) |
| DA88 | - | DA8F | Error codes USB LIGHTRM / HIDERM |
| DA90 |  |  | USB LIGHTRM entry |
| DA93 |  |  | USB HIDERM entry |
| DA90 | - | DAD6 | USB LIGHTRM / USB HIDERM handling |
| DAD7 | - | DB0B | LIGHTRM |
| DB0C | - | DBBA | HIDERM |
| DBBB |  | DD5C | RENUMBER |
| DD5D | - | DD88 | Clear all character shapes from line 9 |
| DD67 | - | DD88 | Clear all character shapes |
| DD89 | - | DDBE | USB DCHAR |
| DDBF | - | DDEE | USB CPOKE |
| DDEF | - | DDFF | spare |
| DE00 |  |  | Return from calculation routine |
| DE01 | - | DE02 | Select calculation routine RD = DB01 RF is 16 bit input for multiply R9, B and C used in calculation routines as pointers to variables |
| DE03 | - | DE59 | Multiply, call via SEP D 03 var1 Result RF = var2 Result (RC)= var1(R9)*var2 Variables: 87 (BE84-BE87), 8b, 8f, 93 etc.) 94-97 USED as addition factor in multiply Routine does not work with negative numbers |
| DE5A | - | DE72 | Add, call via SEP D 5A var1 var2 Result Result(RC)=var1(R9)+var2(RC) |
| DE73 | - | DE88 | Sub, call via SEP D 73 var1 var2 Result Result(RC)=var1(R9)-var2(RC) |
| DE89 | - | DE9D | Multiply * 2, call via SEP D 89 var1 Result Result(RC)=var1*2 Works for negative numbers in var1. |
| DE9E | - | DEA5 | USB SHAPE |
| DEA6 | - | DEB5 | USB FLASH |
| DEB6 | - | DEE1 | USB PPOKE |
| DF0D | - | DF35 | spare |
| DF36 | - | DF3F | Line numbers 10, 100, 1000, 10000, FFFF for USBHIDE RM space calculations |
| DF40 | - | DF80 | USB GRAPH screen details Graph 0 (DF40) START LOC: C1E2/F9E2, X: 38*6=228 (#E4), Y: 12*9=108 (#6C), Y offset = 0, char height=9, number of char per line 40 / #28 Graph 1 (DF48) START LOC: C208/FA08, X: 40*6=240 (#F0), Y: 13.5*16=216 (#D8), Y offset = 8, char height =16, number of char per line 40 / #28 Graph 2 (DF50) START LOC: C0DC/F8DC, X: 20*6=120 (#78), Y: 12*9=108 (#6C), Y offset = 0, char height =9, number of char per line 20 / #14 Graph 3 (DF58) START LOC: C078/F878, X: 20*6=120 (#78), Y: 6.75*16=108 (#6C), Y offset = 4, char height =16, number of char per line 20 / #14 Graph 4 (DF60) START LOC: C1E2/F9E2, X: 38*6=228 (#E4), Y: 12*8=96 (#60), Y offset = 0, char height =8, number of char per line 40 / #28 Graph 5 (DF68) START LOC: C1E0/F9E0, X: 40*6=240 (#F0), Y: 13*16=208 (#D0), Y offset = 0, char height =16, number of char per line 40 / #28 Graph 6 (DF70) START LOC: C0DC/F8DC, X: 20*6=120 (#78), Y: 12*8=96 (#60), Y offset = 0, char height =8, number of char per line 40 / #14 Graph 7 (DF78) START LOC: C079/F879, X: 18*6=108 (#6C), Y: 6.75*16=108 (#6C), Y offset = 4, char height=16, number of char per line 40 / #14 |
| DF81 | - | DFFF | USB PLOT, LINE, CIRCLE character list, pointed by M(BFFB) + DF80 |

## SB RAM Bank 8-12 (C000 - DFFF)

Not used by SB FW and as such available for user programs.

## SB RAM Bank 13 & 14 (C000 - DFFF)

| C000 | - | DFFF | Used by commands DISKCOPY and FILECOPY |
| --- | --- | --- | --- |

## SB RAM Bank 15 (C000 - DFFF)

| C000 | - | D5FF | RAM swap area, mainly used in DOS commands as well as USB GRAPH, PLOT, LINE & CIRCLE for storage of screen content |
| --- | --- | --- | --- |
| DB0A | - | DB0F | F&M Disk Monitor data storage |
| DB10 | - | DC3C | Spare |
| DC40 | - | DC7F | F&M Monitor data storage |
| DC80 | - | DCE0 | CTNL X and V buffer |
| DCFE | - | DCFF | Pointer to current CNTL R buffer |
| DD00 | - | DFFF | CNTL R buffer |

## SB FW ROM (E000 - E7FF)

| E000 | - | E00F | Data table for joystick handling |
| --- | --- | --- | --- |
| E010 | - | E012 | DOS command entry which will call USB command entry at F816. |
| E013 | - | E015 | USB HSWEB for use from external SW (call to E6AA) |
| E016 | - | E018 | USB MON ‘register check' call (call to E681) |
| E019 | - | E01B | NVPUT: R8.1 SW ID, source = RC, R8.0 = number of bytes (call to E66D) |
| E01C | - | E01E | NVGET: R8.1 SW ID, dest = RC, R7.0 = 2 (call to E677) |
| E01F | - | E10A | Updated interrupt routine including printing of clock if needed and JOY handling. |
| E10B | - | E113 | Part of command line input routine, checking if USB SCREEN (42A8 != 0) is active. If so skip printing of ‘:’ |
| E115 | - | E146 | Print error in TEXT via C10B routine in bank 1 |
| E147 | - | E156 | Return to slot stored on BFFE |
| E157 | - | E16D | Write NVRAM location F300 + M[R6] |
| E16E | - | E17F | Read NVRAM location F300 + M[R6] |
| E180 | - | E189 | Part of line input routine printing a ‘?’ followed by a byte 0 character. |
| E18A | - | E202 | Store VOLUME value from NVRAM to 41C9 Switch in bank 15 and reset CNTL X/V and R buffers. Get screen/line editor info from NVRAM and store on 42A8. Find PRINTER (standard or thermal) CARD, store slot code on BEFD. Select bank 1 and call DDD8, which sets USB COLOR, USB CHAR and auto boot 80 column |
| E203 | - | E214 | Auto boot 80 column CARD |
| E215 | - | E2AF | If 80 column boot ongoing: give WARM BOOT message if applicable, give BASIC start-up message for 80/40 column modes. If needed do a call to FCF8 for a DOS NEW |
| E2B0 | - | E308 | Handling of empty line and string in INPUT integer command |
| E309 |  | E327 | Check if NVRAM is working correctly Return: D=0, OK D=FF, error |
| E328 | - | E33D | String assignment handling, allowing A$=USB commands |
| E33E | - | E34C | Part of LET routine, added check is on both CARD and USB statements to allow A=USB commands. |
| E34D | - | E35C | Part of PRINT routines, to allow USB commands to print return values. |
| E35D | - | E36C | Part of IF handling to allow USB commands to be used in IF statements. |
| E36D | - | E372 | Part of RUN code; call E3A0 to handle CLOCK off during RUN and CALL original RUN code at 1F76 |
| E373 | - | E378 | Part of CALL code; call E3A0 to handle CLOCK off during RUN and CALL original CALL code at 2C00 |
| E379 | - | E37E | Part of USR code; call E3A0 to handle CLOCK off during RUN and CALL original USR code at 2C03 |
| E37F | - | E3CE | CLOCK off during RUN/CALL handling. If F3F7 contains invalid value do nothing. If b8=1 reset it to 0. |
| E3A0 | - | E3CE | Switch clock off during RUN / CALL |
| E3CF |  | E470 | Part of LIST code to properly format USB commands |
| E471 | - | E49A | Part of error text routine to handle slot handling if printer or 80 column is active |
| E49B | - | E505 | Store current line in CNTL R buffer (triggered on ‘CR’) At end of routine if R7.0 = 0 set RF.1 to 8D to force an empty line in screen editor mode to come back on next line without error code |
| E506 | - | E54D | CNTL R routine (called when CNTL R is pressed) |
| E54E | - | E55D | Get current CNTL R buffer (from bank 15, DCFE) and return location in RE. |
| E55E | - | E569 | Select slot as stored on BF42 |
| E56A | - | E583 | Store new CNTL buffer location (RE) to bank 15, DCFE. If no RAM found RE=4000 |
| E584 | - | E590 | Call routine on 42A3 with slot as in D; always return to slot 10. |
| E591 | - | E5D4 | Call disk routine Input: address: M[R6]+M[R6+1] return slot m[R6+2] |
| E5D5 | - | E5EA | Select disk card |
| E5EB | - | E5FE | Error code routine which will return as from a normal subroutine call Input: M[R6]= error code number |
| E5FF | - | E615 | Check on WARM boot possibility Return: 0=WARM NOT 0=COLD |
| E616 | - | E620 | Check if 80 column card is active Return: NOT 0=80 column active 0=80 column NOT active |
| E621 | - | E635 | Reset F3ED bit 5, printer off on error code |
| E636 | - | E644 | Set slot back to BFFE and call 2E25 |
| E645 | - | E654 | Set slot back to BFFE + Error code routine Input M[R6] = error code This routine DOES NOT set R8 back to entry value; i.e. only use from CARD routine |
| E655 | - | E66C | USB CARD F search for slot routine |
| E66D | - | E676 | NVPUT: R8.1 SW ID, source = RC, R8.0 = number of bytes (call to bank 0, slot 10, D457) |
| E677 | - | E680 | NVGET: R8.1 SW ID, dest = RC, R7.0 = 2 (call to bank 0, slot 10, D562) |
| E681 | - | E686 | USB MON ‘register check' call (call to bank 4, slot 90, D50E) |
| E687 | - | E69F | Part of EDIT command, check command line to make sure a valid argument is specified like for example (). |
| E6A0 | - | E6A9 | HSWEB for use from USB commands (call to bank 0, slot 10, DD58) |
| E6AA | - | E6B8 | HSWEB for use from external SW |
| E6B9 | - | E6C6 | Call DE48 in bank 0. |
| E6C7 | - | E6D3 | Updated print routine, on B1 / EF1 store character on screen directly, if not store it in print buffer for printing via interrupt routine. |
| E6D4 | - | E6E3 | Called on line buffer overflow, check is done to see if USB BROWSER is active (42A8 = 2) if so continue otherwise give error code 27 |
| E6E4 | - | E6F2 | Called on CNTL S press, if USB BROWSER is active ignore otherwise call CNTL S routine to clear screen |
| E6F3 | - | E713 | Called on cursor down, if USB BROWSER is active ignore otherwise call scroll routine |
| E714 | - | E71A | RENUMBER call to bank 7 |
| E71B | - | E7FF | spare |

## EXPANSION ROM (E800 - EFFF)

All changed locations compared to the original EXPANSION ROM are listed. Note that the original EXPANSION ROM also had a feature which disabled COMX ROM location 1000-17FF and selected E000-E7FF instead. These locations are not listed but are listed as part of the COMX ROM chapter. E000-E7FF is used for SB FW instead.

| E812 | - | E816 | End part of CARD routine which will call routine on EBA2 which will check if a PR or LET statement was used for the CARD command. If so a call is made to 2E25 to return the value to BASIC. |
| --- | --- | --- | --- |
| E83E | - | E844 | Start of CARD routine, added a check if PR or LET statements was used if so branch to EBB1 to handle those CARD statements. |
| E845 | - | E846 | NOP; NOP |
| E847 | - | E867 | Check CARD sub command: B -> EA69 (was EA6D in original ROM) F -> EBD5 (new) P -> E9AA (not changed) Q -> EB0A (not changed) S -> EB57 (not changed) T -> E8FB (not changed) Any other value branches to EC9D to give an error message (5A / decimal 90) |
| E868 | - | E86C | F&M Screen editor adaptation |
| E897 | - | E8AE | F&M Screen editor adaptation (branch to EC9D changed to ECA1) |
| E985 | - | E9A9 | Removed error text message ‘NO THERMAL PRINTER CARD’ replaced by routines below. |
| E985 | - | E987 | Call error code routine with error 5A / decimal 90 to replace text message. |
| E988 | - | E9A9 | F&M Screen editor adaptation |
| EA50 | - | EA6C | Removed error text message ‘NO PRINTER CARD’ replace by routines below. |
| EA50 | - | EA52 | Call error code routine with error 5A / decimal 90 to replace text message. |
| EA53 | - | EA6B | Check if screen editor is active (42A8 = 0). If not active execute line editor code at EA59-EA62. If active execute code at EA63-EA6B |
| EA6D | - | EB09 | Removed (rewritten) CARD B code with below routines |
| EA69 | - | EA8C | New CARD Bx code |
| EA8D | - | EA97 | Print FW version, EA91/EA92/EA93 contains the number |
| EA98 | - | EADA | Fetch ‘x’ value in CARD Fx. X can be 0 to FE |
| EA9B | - | EADA | Fetch ‘x’ value in CARD Bx. X can be 0 to E |
| EA9E | - | EADA | Fetch ‘x’ value in CARD Sx. X can be 0 to 4 |
| EAED |  |  | 1 byte spare |
| EAFB | - | EB09 | New CARD B code |
| EB16 | - | EB18 | End CARD Q routine: branch to FD4C to set 42AD = 85, call 1A6C and branch to E800 (original part which is end of CARD routine) |
| EB3B |  |  | Part of bank change routine changed E0 to E1 so all 4 SB bank bits are used |
| EB57 | - | EC32 | Removed (rewritten) CARD S code with below routines |
| EB57 | - | EBA1 | New CARD Sx code |
| EBA2 | - | EBB0 | End part of CARD routine, to check if a PR or LET statement was used for the CARD command. If so a call is made to 2E25 to return the value to BASIC. |
| EBB1 | - | EBB5 | Check LET CARD commands F -> EBC0 Other (S) -> EBB6 |
| EBB6 | - | EBBF | Continue LET CARD command check in bank 6, slot D0 address DB74. |
| EBC0 | - | EBD0 | LET CARD F code, search for indicated card via E655 routine, then call LET CARD F routine in bank 6, slot D0 address DBAC |
| EBD1 | - | EBD4 | 4 bytes spare |
| EBD5 | - | EBE0 | New CARD Fx code |
| EBE1 | - | EC32 | F&M Screen editor adaptation |
| EC9D | - | ECB7 | Removed error text message ‘SYNTAX ERROR’ replaced by routines below. |
| EC9D | - | ECA4 | Error code calls 5A and 5F |
| ECA5 | - | ECA7 | 3 bytes spare |
| ECA8 | - | ECB1 | F&M Screen editor adaptation - Down |
| ECB2 | - | ECB7 | 6 bytes spare |
| ECB8 | - | EDA5 | Removed CARD M and V code |
| ECB8 | - | EFFF | F&M Screen editor adaptation (some details / changes below) |
| ECBB | - | ECD3 | Shape line 10 to character number for use screen editor |
| ED90 | - | EDA7 | Jump table for keys: ED90 – ED91: 041C Up ED92 – ED93: EDEA right ED94 – ED95: EDA8 Down ED96 – ED97: 0357 Left ED98 – ED9E: 0322 CNTL C / CR ED9E – ED9F: E6E4 CNTL S |
| EDDD | - | EDDF | Call new scroll routine at FC1A |
| EDE0 | - | EDE6 | F&M Screen editor adaptation, code moved from E861 to EDD0-EDE6 |
| EDE7 | - | EDE9 | Call to called on ‘down’ on last screen row to check is USB BROWSER is active, if not screen is scrolled |
| EE61 | - | EE62 | Part of CNTL S routine which is change to call FD1C to enable TV out (if it was disabled) and reset DHEIGHT and WIDTH settings to normal. |
| EE8E | - | EE90 | Part of cursor shape routine, calling FD0A to select line 8/9 for cursor depending on NTSC/PAL machine |
| EEC4 | - | EEC9 | Check for CNTL keys; continue on F9A8 to check different key presses |
| EECA | - | EEDC | F&M Screen editor code moved from EEC4-EED6 |
| EEDD | - | EEE2 | Check for CNTL R, if pressed call CNTL R routine at E506 |
| EEE3 | - | EEEF | F&M Screen editor code rewritten to fit in EEE1-EEEF |
| EF18 |  |  | Changed F&M Screen editor branch to E3C8 to the actual address 13C8 |
| EF25 |  |  | Changed F&M Screen editor branch to E3D3 to the actual address 13D3 |
| EF4A | - | EF4C | Call routine on E49B to store current line in CNTL R buffer (triggered on ‘CR’) |
| EF54 |  |  | Corrected branch to EADB to fit changed code |
| EF5D | - | EF5E | Added RF.0 storage on stack |
| EF55 | - | EFA4 | Read current screen location Return: Character in R8.0 and on 43F9 |
| EFFE | - | EFFF | Call EDE0 instead of E861 as routine was moved |

## NVRAM & RTC (F000 - F3FF)

| F000 | - | Fxxx | User area. This area can be used by any user or user program. No defined format is available so any address location can be filled as desired. USB NVPOKE can be used to store data and COMX BASIC PEEK can be used to retrieve data. Fxxx is defined via USB NVSTART. |  |
| --- | --- | --- | --- | --- |
| Fxxx | - | F3E7 | Software area. This area can be used by any software. The area is formatted so every software program can find stored data back. USB NVPUT, NVGET, NVIGET, NVSGET, NVCLR and NVDEL can be used to store, retrieve or manipulate data to/from this area |  |
| F3E8 |  |  | NVRAM SW area start. Start = F000h + (value << 2) | 0 = F000h |
| F3E9 |  |  | SCREEN, COLOR & CTONE b7: not used b6/b5: colb1/colb0 b4: not used b3: ctone b2-b0: background color | E0h |
| F3EA |  |  | b7/b6: Last color shape mask, copied from 41CB during COLOR routine b5/b4: saved color shape mask (USB COLOR) | F0h |
| F3EB |  |  | Printer settings (also copied to 41B0h) b7: SHAPE flash 1 = on, 0 = off b6: Printer CNTL characters; 1 = normal, 0 = hex b0-b5: number of stop bits 0-63 | 42h = 2 stop bits, normal CNTL and no SHAPE flash |
| F3EC |  |  | NVRAM initialized (A5h = initialized) |  |
| F3ED |  |  | b6: online mode; 1 = on, 0 = off b5: printer off on error code; 1 = yes, 0 = no b4: printer ‘on’ state before command; 1 = on, 0 =off b0-3: Volume | 44h = online mode = on, Volume level 4 |
| F3EE |  |  | Serial Printer settings (also copied to 41B1H/41B2H) b6: line feed suppression; 1 = yes, 0 = no b5: parity type; 1 = even, 0 = odd b4: parity; 1= yes, 0 = no b2-b3: number of data bits 00=5, 10=7 or 11=8 b0-b1: Baud rate 00=1200, 01=600, 10=300, 11=110 | 0Dh = Baud rate 600, 8 data bits, No parity and no LF suppression |
| F3EF |  |  | Serial Printer settings (also copied to 41B3h) CR pause 0-255 | 5 = CR pause 5 |
| F3F0 |  |  | b7: Logo tune; 1 = on, 0 =off b6: 80 column auto boot ; 1 = on, 0 =off b5: Boot message; 1 = on, 0 =off b4: Line editor; 0 = on, 1 =off (copied to 43F8H) b3: Printer TV; 1 = on, 0 =off (copied to b7 41b0h) b2: Printer keyboard output; 1 = on, 0 =off b1-b0: USB CHAR set | B4h = Logo tune: on 80 column auto boot: off Boot message: on Screen editor: on Printer TV: off Printer keyboard: on Character set: Standard COMX characters |
| F3F1 |  |  | Date separator character (-, / etc) | 2Fh = / |
| F3F2 |  |  | Date format xx (xx/yy/zz) FCH = day, FDH = month, FEH = year | FCh = day |
| F3F3 |  |  | Date format yy (xx/yy/zz) FCH = day, FDH = month, FEH = year | FDh = month |
| F3F4 |  |  | Date format zz (xx/yy/zz) FCH = day, FDH = month, FEH = year | FEh = year |
| F3F5 |  |  | Time format; 12h (12 hour) or 24h (24 hour) | 24h = 24 hour |
| F3F6 |  |  | NVRAM check field, used by SB FW to check is NVRAM is available |  |
| F3F7 |  |  | Clock display; 1 = on when COMX is not ’running’ any program 2 = always on 0 = off b8: 1 when RUN / CALL or USR is ‘running’ | 0 = clock display off |
| F3F8 | - | F3FF | RTC |  |

## Character Memory (F400 - F7FF)

CDP 1870 Character Memory

## SB FW ROM / Page Memory (F800 - FFFF)

When writing data to F800 – FFFF area it will be used as CDP 1870 Screen page memory, when reading data below will be seen

| F800 | - | F801 | BR16, USB Command entry; used from C010 in all banks |
| --- | --- | --- | --- |
| F802 | - | F803 | Set slot back to M[BFFE] and pull registers from stack (end USB command), if printer is active set slot to M[BFFD] (call F83A) |
| F804 | - | F806 | EDIT function in screen editor (call 1052) |
| F807 | - | F80D | Read location from slot x. Always CALL this routine via SEP x to F808! Input: M[R2]=slot M[R2+1]=return slot Output: D= M[RC] |
| F80E | - | F815 | Store to location M[RC] in slot x. Always CALL this routine via SEP x to F80F! Input: M[R2]=slot M[RC]=M[R2+1] M[R2+2]=return slot |
| F816 | - | F839 | USB Command entry which will switch in bank 0 and call command entry routines at C915. |
| F83A | - | F859 | Set slot back to M[BFFE] and pull registers from stack (end USB command), if printer is active set slot to M[BFFD] |
| F83F | - | F859 | Set slot back to M[BF42] and pull registers from stack |
| F85A | - | F8E3 | USB PLOAD/PSAVE routines |
| F8E4 | - | F93B | HEX / DEC Routine 1 |
| F8E9 | - | F93B | HEX / DEC Routine 1 |
| F93C | - | F95B | Part of USB PLOAD,R command: set slot back to M[BF42] and pull registers from stack (as for end USB command). Then switch off clock if needed and execute ‘CALL’ by calling sub on 42A3. |
| F95C | - | F969 | Force bank = 0 but leave slot as selected before |
| F96A | - | F98A | If printer is active set slot to M[BFFD] otherwise M[BFFE] |
| F975 | - | F98A | Set slot back to code on BFFD (printer slot) |
| F978 | - | F98A | Set slot back to code on BFFE (selected slot at USB/DOS command entry) |
| F97B | - | F98A | Set slot back to code on BF42 (current selected slot) |
| F98B | - | F9A7 | Part of USB PLOAD,R command: set slot back to M[BF42] and pull registers from stack (as for end USB command). The execute ‘RUN’ by calling routine on E36D. |
| F9A8 | - | F9B9 | CNTL check routine, if no CNTL key pressed continue at EECA: CNTL E -> FB92 CNTL W -> FBB0 CNTL X -> F9BA CNTL V -> FA15 |
| F9BA | - | FA14 | CNTL X routine |
| FA15 | - | FA54 | CNTL V routine |
| FA55 | - | FA8E | Print char (D) on screen and scroll if needed, used by CNTL V, R routines |
| FA8F | - | FAA8 | Step current cursor position and check for end of line/screen, used by CNTL V, R, X, E routines |
| FAA9 | - | FAB0 | Handle bug in READ feature which crashed if no DATA statements are available. |
| FAB1 | - | FAD3 | Clear line from current position |
| FAD4 | - | FAE6 | Search for first character in current input line (i.e. search for ‘0’) |
| FAE7 | - | FAFD | Step current position one position back |
| FAFE | - | FB45 | Print current CNTL R buffer to screen |
| FB46 | - | FB6B | Check on invalid line numbers, i.e >= FFFF. Introduced to fix bug in original COMX BASIC which crashes on line number 65535. |
| FB6C | - | FB91 | Part of EDIT routine to handle different EDIT behavior if screen editor is active. If active the EDIT line number is just printed on screen, if not active normal original EDIT call is made. |
| FB92 | - | FBA4 | CNTL E routine |
| FBA5 | - | FBAF | Print character on cursor position back on screen (i.e. remove cursor) |
| FBB0 | - | FBD2 | CNTL W routine |
| FBD3 | - | FBD8 | Error code routine Input: M[R6] = error code |
| FBD9 | - | FBDA | Disk routine: SEP RE / SEP R5 |
| FBDB | - | FBF2 | COPY TO/FROM bank x (1) Input: R7 = source start RF = length R8 = destination RE.0 = return slot RE.1 = destination slot RA.1=source slot |
| FBDD | - | FBF2 | COPY TO/FROM bank x (1) R7 = source start RF = length R8 = destination RE.0 = return slot RA.1 = destination slot RE.1=source slot |
| FBF3 | - | FBF7 | Call DOS routine in RAM (B700) |
| FBF8 | - | FC35 | New scroll routine to handle clearing of clock |
| FC36 | - | FC69 | Call subroutine in other bank Input: M[P+1]=slot M[P+2/3]=address |
| FC51 | - | FC69 | Call subroutine in other bank Input: M[R2]=slot M[R2+1]=RF.1 M[R2+2]= return slot |
| FC6A | - | FCAA | Check if printer is active, if active select printer, branch to M[R6+1/R6+2] and switch back to slot on M[R6]. If no printer active just branch to M[R6+1/R6+2]. |
| FCAB | - | FCBC | Call to E621, to check printer off on error code bit, if set reset to 0. If needed switch off printer. Perform line feed including printer checks. |
| FCBD | - | FCD5 | COPY TO/FROM bank x (2) Input: R7 = source end RF = length R8 = destination RE.0 = return slot RE.1 = destination slot M[R2] = source bank x |
| FCBF |  | FCD5 | COPY TO/FROM bank x (2) R7 = source end RF = length R8 = destination RE.0 = return slot RA.1 = destination slot M[R2] = source bank x |
| FCD6 |  | FCDB | Part of PLOAD routine, call FCE2 to do an INP 1 which will re-activate EF handling for tape. |
| FCDB | - | FCE1 | Part of DLOAD routine, call FCE2 to do an INP 1 which will re-activate EF handling for tape. |
| FCE2 | - | FCE8 | INP 1 which will re-activate EF handling for tape. |
| FCE9 | - | FCF7 | Find card Input: Card id stored on RC = BF41 return to slot M[R6] |
| FCF8 | - | FD04 | Find FDC and call DOS NEW |
| FD05 | - | FD09 | Find FDC, return D = 0 if not found |
| FD0A | - | FD1B | Select line 8/9 for cursor depending on NTSC/PAL machine |
| FD1C | - | FD38 | Part of CNTL S routine to enable TV out (if it was disabled) and reset DHEIGHT and WIDTH settings to normal. |
| FD39 | - | FD4B | If 80 column is booted set 42AD = 0D and call ECBB, if not call ECB8 |
| FD4C | - | FD55 | End CARD Q routine, added setting of 42AD = 85, call 1A6C and branch to E800 (original part which is end of CARD routine) |
| FD56 | - | FD66 | Cursor COL40 switch |
| FD67 | - | FD83 | Cursor COL80 switch |
| FD84 | - | FD90 | Start is on FD.., print command on screen as stored on memory pointed by RC. Used by LIST routine. |
| FD91 | - | FD9B | String assignment handling, allowing A$=USB commands. If command input is USB branch to 2A0E otherwise 2A08. |
| FD9C | - | FDFA | Part of line input routine converting lower case characters to capitals in commands. |
| FDFB | - | FE47 | Used by PR and IF handling to allow USB commands to be used: Checks if first char is B (BIN or BLOAD), C (CD), D (DATE, DLOAD, DEL), H (HEX), U (URL, URLGET), N (NVGET, NVPUT, NVSGET). If first char is a C also second char is checked on ‘D’ to make a difference between USB COMP which returns an INT and CD which returns a STR. If first char is an N also 3rd char is checked on ‘G’, ‘P’ and ‘S’ to make sure NVIGET is not seen as returning a string Last a check is performed on sub command code, if it is 98 (PLOAD), A1 (DLOAD) or AF (TIME) also returning a STR will be allowed |
| FE48 | - | FE5D | SWAP from bank x to RAM Input: R7 = source start RF = length R8 = destination RE.0 = return slot M[R2]= bank x |
| FE5E |  | FE81 | Part of COLOR routine, call to 0C80 and after that set the last color shape mask back to NVRAM (b7/b6 on F3EA). |
| FE82 | - | FE98 | Copy BE83 buffer to 4200 to return error code |
| FE99 | - | FEA7 | Error code routine, if R7.0 = 2 call error code routine which ‘returns’ on E64F |
| FEA8 | - | FEBD | Check command buffer for end of command, return 0 it end of command |
| FEBE | - | FEDC | Check if USB GRAPH is active if so re-shape and set normal screen. Then jump to 80 column check. |
| FEDD | - | FEF1 | CPOS check if DWIDTH is active |
| FEF2 | - | FF01 | ? Adaptation to allow line numbers between @FF00-@FFFE in renumber |
| FF02 | - | FF49 | spare |
| FF4A | - | FF4F | INPUT ‘0’ data |
| FF50 | - | FF51 | Data: ‘SB’ text used for check if data is valid to load with RLOAD. i.e. a compare is done if ‘SB’ is stored in the end of the bank. |
| FF52 | - | FF64 | F8DF Text: ‘W = WARM START’ |
| FF63 | - | FF70 | F890 Text: ‘SUPER BOARD’ |
| FF71 | - | FF83 | F92E Text: ‘SUPER BOARD 2014’ |
| FF84 | - | FF8E | F946 Text: ‘ED KEEFE’ |
| FF8F | - | FFA3 | F955 Text: ‘MARCEL V. TONGEREN’ |
| FFA4 | - | FFAE | F996 Text: ‘1985 F&M’ |
| FFAF | - | FFBE | F97F Text: ‘SCREEN EDITOR’ |
| FFBF | - | FFCF | F9 BB Text: ‘© 1983 C O M X’ |
| FFD0 | - | FFE6 | F9CC Text: ‘WORLD OPERATIONS LTD’ |
| FFE7 |  |  | End code Text #FF, possibly used for something else? |
| FFE8 | - | FFF7 | NVRAM system area defaults |
| FFF8 | - | FFFF | Store to location M[RF] in slot x. Always CALL this routine via SEP x to FFF9! Input: M[R2]=slot M[RF]=M[R2+1] M[R2+2]=return slot |

# APPENDIX C – PC <-> COMX HEADERS

This chapter lists all headers used for USB communication between the PC SW and COMX

## Standard Header (COMX <-> PC)

| Address | Bytes | Address Description | Value | Value Description |
| --- | --- | --- | --- | --- |
| 0h | 1 | Command type | 0 | None |
|  |  |  | 1 | Save |
|  |  |  | 2 | Load |
|  |  |  | 3 | Get first CAT content |
|  |  |  | 4 | Get next CAT content |
|  |  |  | 5 | CD - Change directory |
|  |  |  | 6 | MKDIR |
|  |  |  | 7 | RMDIR |
|  |  |  | 8 | DEL |
|  |  |  | 9 | Fetch time & date |
|  |  |  | 12h, 14h, 16h, 1Ah | Used in image header |
|  |  |  | 18h | COMP, Compare files |
|  |  |  | 19h | URL |
|  |  |  | 42h | DLOAD |
|  |  |  | 81h | Save and overwrite existing file |
|  |  |  | 82h | Load continue |
|  |  |  | FFh | Cancel command |
| 1h | 18 | Program or directory name |  | Name in ASCII characters |
| 13h | 1 | Result | 0 | File found |
|  |  |  | ADh, AEh, AFh | Used in image header |
|  |  |  | F3h | URL not found |
|  |  |  | F4h | No more data found |
|  |  |  | F5h | Server error |
|  |  |  | F6h | Network error |
|  |  |  | F7h | File open |
|  |  |  | F8h | File error |
|  |  |  | F9h | File size > 8K |
|  |  |  | FAh | File size > 64K |
|  |  |  | FBh | File size < 8K |
|  |  |  | FCh | File size < 64K |
|  |  |  | FDh | File type error |
|  |  |  | FEh | Address error |
|  |  |  | FFh | File NOT found |
| 14h | 2 | Actual file length (excl. header) |  |  |

| 16h | 1 | Program type | 1 | .comx machine code |
| --- | --- | --- | --- | --- |
|  |  |  | 2 | .comx ‘old’ regular save/load (for backward compatibility reasons only) |
|  |  |  | 3 | .comx F&M basic save/load |
|  |  |  | 4 | .comx ‘old’ and incorrect regular data load (for backward compatibility reasons only) |
|  |  |  | 5 | .comx regular data save/load |
|  |  |  | 6 | .comx regular save/load |
|  |  |  | 7h to 9h | reserved for .comx format |
|  |  |  | 10h | .bin |
|  |  |  | 11h | .txt (memory dump) |
|  |  |  | 12h | .img |
|  |  |  | 13h | .ram |
|  |  |  | 14h | .bin, .txt, img, .ram, .comx |
|  |  |  | 20h | .comx.bak |
|  |  |  | 21h | NVSAVE / nvram.bin |
|  |  |  | 22h | SYSSAVE / system.bin |
|  |  |  | 23h | NVSYNC |
|  |  |  | 24h | URL |
|  |  |  | 25h | URL INPUT |
|  |  |  | 30h | .bin.bak |
|  |  |  | 31h | .txt.bak |
|  |  |  | 32h | .img.bak |
|  |  |  | 33h | .ram.bak |
|  |  |  | 34h | .bin.bak, .txt.bak, img.bak, .ram.bak, .comx.bak |
|  |  |  | b7 = 1 | BLOAD/BSAVE active |
| 17h | 2 | Start address |  | Basic | Machine code | Data |
|  |  |  |  | DEFUS | Start | String |
| 19h | 2 | End address |  | EOP | End-1 | Array |
| 1Bh | 2 | Exec address |  | String/Array/EOD | Exec | EOD |
| 1Ch | 18 | Filename 2 |  | Name in ASCII characters (used for USB COMP) |
| 2Fh | 1 | Category |  | Not used |
| 30h | 1 | Case type | 1 | Standard COMX characters (upper case ‘default’) |
|  |  |  | 2 | Lower case ‘default’ standard COMX characters on ‘SHIFT’ |
|  |  |  | 3 | Upper case ‘default’ and lower case characters on ‘SHIFT’ |
|  |  |  | 4 | Lower case ‘default’ and upper case characters on ‘SHIFT’ |
| 31h | 1 | High byte start load |  |  |
| 32h | 1 | BLOAD/BSAVE type | 30h | One RAM Bank x |
|  |  |  | 31h | RAM Banks 8 to 15 |
|  |  |  | 32h | RAM Banks 8 to 15 Continue |
| 33h | 2 | BLOAD/BSAVE length | 2 |  |
| 35h | 3 | FW build number |  | FW build (3 ascii values) |

## CD Header (PC -> COMX)

| Address | Bytes | Address Description | Value | Value Description |
| --- | --- | --- | --- | --- |
| 0h | 1 | Result | FFh | Directory not found |
| 1h | 126 | Full path |  | Path name in ASCII characters |
| Last byte | 1 | End code | 0 |  |

## URL,”url” Header (COMX -> PC)

| Address | Bytes | Address Description | Value | Value Description |
| --- | --- | --- | --- | --- |
| 0h | 1 | Command type | 19h | USB URL |
| 1h | 126 | URL |  | URL name in ASCII characters |
| Last byte | 1 | End code | 0 |  |

## URL (x) and URLLINK (x) Header (COMX -> PC)

| Address | Bytes | Address Description | Value | Value Description |
| --- | --- | --- | --- | --- |
| 0h | 1 | Command type | 19h | USB URL |
| 1h | 1 | Command | < 32 | 0 = Normal USB URL / LINK 1 = PAGE BACK 2 = GO TO HOME 3 = SET HOME 4 = GO TO BOOKMARK 5 = SET BOOKMARK 6 = HELP |
| 2 | 2 | Screen number | 0-65535 | USB URL: Data screen number |
| 2 | 1 | Bookmark | 0-9 | Bookmark number |
| 2 | 1 | Link | 0-255 | USB URLLINK: New link number, link number 0 = default page |

## CAT Header (PC -> COMX)

| Address | Bytes | Address Description | Value | Value Description |
| --- | --- | --- | --- | --- |
| 0h-1Bh |  |  |  | Entry 1 + x Every header contains 4 directory entries and is send until no more entries are available (entry number = 0) |
| 0h | 1 | Entry number | 0 | No more entries |
|  |  |  | 1 – FEh | Directory entry number of specified file |
|  |  |  | FFh | Directory name |
| 1h | 18 | Program or directory name |  | Name in ASCII characters |
| 13h | 1 | Result | 0 | File found |
|  |  |  | ADh | Format error SS / SD |
|  |  |  | AEh | Format error SS / DD |
|  |  |  | AFh | Format error DS / SD |
|  |  |  | F5h - FEh | Used in standard header |
|  |  |  | FFh | File NOT found |
| 14h | 1 | Size | 0 - FFh | File size if > 255 KB; otherwise 0 |
| 16h | 1 | Program type | 1 | .comx machine code |
|  |  |  | 2 | .comx ‘old’ regular save/load (for backward compatibility reasons only) |
|  |  |  | 3 | .comx F&M basic save/load |
|  |  |  | 4 | .comx ‘old’ and incorrect regular data load (for backward compatibility reasons only) |
|  |  |  | 5 | .comx regular data save/load |
|  |  |  | 6 | .comx regular save/load |
|  |  |  | 7h to 9h | reserved for .comx format |
|  |  |  | 10h | .bin |
|  |  |  | 11h | .txt (memory dump) |
|  |  |  | 12h | .img |
|  |  |  | 13h | .ram |
|  |  |  | 20h | .bak |
| 17h | 2 | Start address |  | Basic | Machine code | Data |
|  |  |  |  | DEFUS | Start | String |
| 19h | 2 | End address |  | EOP | End-1 | Array |
| 1Bh | 2 | Exec address |  | String/Array/EOD | Exec | EOD |
| 20h-3Bh |  |  |  | Entry 2 + x |
| 40h-5Bh |  |  |  | Entry 3 + x |
| 60h-7Bh |  |  |  | Entry 4 + x |

## Image file Header (COMX <-> PC)

| Address | Bytes | Address Description | Value | Value Description |
| --- | --- | --- | --- | --- |
| 0h | 1 | Command type | 0 – 9 | Used in standard header |
|  |  |  | 12h | Get track image file |
|  |  |  | 14h | Save track image file |
|  |  |  | 16h | Test image file |
|  |  |  | 18h | Used in standard header |
|  |  |  | 1Ah | Get track image file continue |
|  |  |  | 42h | Used in standard header |
|  |  |  | 81h – 82h | Used in standard header |
|  |  |  | 94h | Save track image and overwrite existing file |
|  |  |  | FFh | Cancel command |
| 1h | 18 | Program or directory name |  | Name in ASCII characters |
| 13h | 1 | Result | 0 | File found |
|  |  |  | ADh | Format error SS / SD |
|  |  |  | AEh | Format error SS / DD |
|  |  |  | AFh | Format error DS / SD |
|  |  |  | F5h - FEh | Used in standard header |
|  |  |  | FFh | File NOT found |
| 14h | 1 | Density | 0 | Single |
|  |  |  | 1 | Double |
| 15h | 1 | Sides | 0 | Single |
|  |  |  | 1 | Double |
| 16h | 1 | Track type | 0 | First track |
|  |  |  | 1 | Second until last -1 |
|  |  |  | 2 | Last track |
| 17h | 1 | Drive & side | 14H | Drive 1 & side 1 |
|  |  |  | 34H | Drive 1 & side 2 |
|  |  |  | 18H | Drive 2 & side 1 |
|  |  |  | 38H | Drive 2 & side 2 |
| 18h | 1 | Track number | 0 to 34 |  |
| 19h | 1 | Side | 0 or 1 |  |
| 30h | 1 | Case type | 1 | Standard COMX characters (upper case ‘default’) |
|  |  |  | 2 | Lower case ‘default’ standard COMX characters on ‘SHIFT’ |
|  |  |  | 3 | Upper case ‘default’ and lower case characters on ‘SHIFT’ |
|  |  |  | 4 | Lower case ‘default’ and upper case characters on ‘SHIFT’ |

# APPENDIX D – ERROR MESSAGES

This chapter lists all known COMX error messages, including the original COMX BASIC, PRINTER, DOS, F&M BASIC and SB error messages

## COMX 35 BASIC Error Messages

| DEC | HEX | ERROR CODE |
| --- | --- | --- |
| 0 | 0 | Program halted by user |
| 1 | 1 | Syntax error in asc or len function |
| 2 | 2 | Array out of range or not dimensioned |
| 3 | 3 | Dimension error |
| 4 | 4 | Defint has illegal ending |
| 5 | 5 | Parentheses missing in argument |
| 6 | 6 | Argument out of range |
| 7 | 7 | Mixed mode calculation encountered |
| 8 | 8 | Divide by zero error, or log of negative number |
| 9 | 9 | Non-executable function encountered |
| 10 | A | Exit command must be used with for/next or gosub/return |
| 11 | B | For/next stack overflow, or for/next executed directly |
| 12 | C | Syntax error in for |
| 13 | D | Gosub stack overflow |
| 14 | E | Unacceptable character in hexadecimal number |
| 15 | F | Floating point number too large to be converted to integer or integer multiply overflow |
| 16 | 10 | Unacceptable operator in conditional statement |
| 17 | 11 | Input or fval cannot be directly executed |
| 18 | 12 | Must have variable or string name in read |
| 19 | 13 | Syntax error in read or input |
| 20 | 14 | Syntax error in len function |
| 21 | 15 | Syntax error in assignment statement |
| 22 | 16 | Missing quote |
| 23 | 17 | Syntax error in list |
| 24 | 18 | No such word found in library |
| 25 | 19 | Syntax error in mid$ function |
| 26 | 1A | Unacceptable variable name found in next statement |
| 27 | 1B | Either a number or a letter is expected |
| 28 | 1C | Missing arithmetic parentheses |
| 29 | 1D | Wrong number of arguments in poke statement |
| 30 | 1E | Unacceptable last character in print statement |
| 31 | 1F | Syntax error in data statement |
| 32 | 20 | No more data found |
| 33 | 21 | No such string found in input statement |
| 34 | 22 | Missing equal sign in assignment statement |
| 35 | 23 | Missing parentheses in string array |
| 36 | 24 | Too many arguments in usr or call |
| 37 | 25 | Syntax error in chr$ function |
| 38 | 26 | Unacceptable character in binary number |
| 39 | 27 | Line buffer overflow |
| 40 | 28 | File not opened for input |
| 41 | 29 | File not opened for output |
| 42 | 2A | Unacceptable line end or non-executable statement |
| 43 | 2B | Stack overflow |
| 44 | 2C | Too many digits in number |
| 45 | 2D | Unacceptable character in number fold |
| 46 | 2E | No such line number found |
| 47 | 2F | Unacceptable operation in if statement |
| 48 | 30 | Memory overflow |
| 49 | 31 | Wrong number of arguments in mod statement |
| 50 | 32 | Program too large for memory |
| 51 | 33 | Argument out of range |
| 52 | 34 | Wrong number of arguments |
| 53 | 35 | Wrong number of arguments |
| 54 | 36 | String variable not defined |
| 55 | 37 | Tape read error |
| 56 | 38 | Tape write error |
| 57 | 39 | File is not a basic program |
| 58 | 3A | File is not basic data |
| 59 | 3B | Reserved |
| 60 | 3C | Reserved |
| 61 | 3D | Reserved |
| 62 | 3E | Rom or rom card not present |
| 63 | 3F | Not enough memory for renumber to operate |
| 64 | 40 | Renumber located line number error |
| 65 | 41 | No such subscript variable defined |
| 66 | 42 | String is over 127 characters |
| 67 | 43 | Number of arguments in color must be 1 |
| 68 | 44 | Number of arguments in screen must be 1 |
| 69 | 45 | Number of arguments in ctone must be 1 |
| 70 | 46 | Number of arguments in volume must be 1 |
| 71 | 47 | Number of arguments in noise must be 2 |
| 72 | 48 | Number of arguments in tone or music must be 3 |

## F&M BASIC V2.00 Error Messages

| DEC | HEX | ERROR CODE |
| --- | --- | --- |
| 73 | 49 | Number of arguments in TEXT must be 1 |
| 74 | 4A | Number of arguments in POINT must be 2 |
| 75 | 4B | Number of arguments in DUMP must be 2 |
| 76 | 4C | Number of arguments in CHAR must be 1 |
| 77 | 4D | Incorrect use of ALPHA |
| 78 | 4E | Line number missing |
| 79 | 4F | TOS not found |
| 81 | 51 | Number of arguments in P-SCR must be 1 |
| 82 | 52 | Not enough memory for P-SCR |
| 83 | 53 | Number of arguments in DEL must be 1 or 2 |
| 84 | 54 | First argument in DEL must be lower than last |
| 85 | 55 | TOS command not recognized |

## PRINTER Error Messages

| DEC | HEX | ERROR CODE |
| --- | --- | --- |
| 80 | 50 | Printer error |

## COMX 35 DOS Error Messages

| DEC | HEX | ERROR CODE |
| --- | --- | --- |
| 100 | 64 | Text file record length is not fixed |
| 101 | 65 | Record number exceeds file size |
| 102 | 66 | Disk read error |
| 103 | 67 | Read or write pointer exceeds file size |
| 104 | 68 | Sector read or write error |
| 105 | 69 | Seek error |
| 106 | 6A | Diskette write protected |
| 107 | 6B | File locked |
| 108 | 6C | Spare |
| 109 | 6D | Spare |
| 110 | 6E | Slash missing |
| 111 | 6F | End of command found |
| 112 | 70 | Work id. Number error |
| 113 | 71 | Record length missing |
| 114 | 72 | More than 8 arrays already exist |
| 115 | 73 | String or array variable error |
| 116 | 74 | Not integer or too large integer exist |
| 117 | 75 | Not a fixed record length file type |
| 118 | 76 | String exceeds record length |
| 119 | 77 | Spare |
| 120 | 78 | Address syntax error |
| 121 | 79 | Drive number argument or syntax wrong |
| 122 | 7A | Not enough disk memory |
| 123 | 7B | Parenthesis missing |
| 124 | 7C | Input file name error |
| 125 | 7D | Comma missing |
| 126 | 7E | Command does not exist |
| 127 | 7F | Syntax error on ‘save’ command |
| 128 | 80 | Quotation mark missing |
| 129 | 81 | File name already opened or exists in directory |
| 130 | 82 | File not found in directory |
| 131 | 83 | No such kind of protection |
| 132 | 84 | More than 5 files already opened |
| 133 | 85 | File name not yet opened |
| 134 | 86 | More than 51 directory entries |
| 135 | 87 | File write protected |
| 136 | 88 | Disk or file non-copyable |
| 137 | 89 | No such handler command code |

## SB Error Messages

| DEC | HEX | ERROR CODE |
| --- | --- | --- |
| 86 | 56 | Only one parameter (B, I, R, T) allowed |
| 87 | 57 | Invalid parameter |
| 88 | 58 | Program will not fit into 8K RAM bank |
| 89 | 59 | Number of arguments in USB MOVE must be 3, 4 or 6 |
| 90 | 5A | Syntax error in CARD statement |
| 91 | 5B | No rtc or nvram found, or nvram not initiated |
| 92 | 5C | No valid data in RAM bank |
| 93 | 5D | Could not delete file |
| 94 | 5E | No data to save |
| 95 | 5F | No disk card or disk not initiated |
| 96 | 60 | Too many parameters |
| 97 | 61 | Nvram write enable error |
| 98 | 62 | Specify date string |
| 99 | 63 | Incorrect date string format |
| 138 | 8A | Incorrect I/O port specified |
| 139 | 8B | Number of arguments in USB OUT must be 2 |
| 140 | 8C | Number of arguments in USB PPOKE or USB NVPOKE must be 2 |
| 141 | 8D | NVPOKE or NVSTART address out of nvram range |
| 142 | 8E | USB command not recognized |
| 143 | 8F | Help for command not found |
| 144 | 90 | Command ROM not detected |
| 145 | 91 | Unknown or incorrect file format |
| 146 | 92 | F&M BASIC not loaded |
| 147 | 93 | File name too long |
| 148 | 94 | No filename specified |
| 149 | 95 | Address range required |
| 150 | 96 | End address required |
| 151 | 97 | Invalid RAM bank |
| 152 | 98 | Invalid directory |
| 153 | 99 | Could not create directory |
| 154 | 9A | Specify start < end address |
| 155 | 9B | Could not delete directory |
| 156 | 9C | Specify start address |
| 157 | 9D | Incorrect line number |
| 158 | 9E | Number of arguments in USB CPOS must be 2 |
| 159 | 9F | Specify start <= DEFUS address |
| 160 | A0 | Program cannot be loaded in F&M BASIC |
| 161 | A1 | Number of arguments in USB NVPUT must be 3 |
| 162 | A2 | NVRAM full, data not stored |
| 163 | A3 | Software ID not found |
| 164 | A4 | Number of arguments in USB NVGET must be 2 |
| 165 | A5 | Number of arguments in USB NVIGET , NVSGET, NVDEL and NVSTART must be 1 |
| 166 | A6 | Requested NVRAM size to small to fit current data |
| 167 | A7 | Software ID should be between 1 and 255 |
| 168 | A8 | Label or date string too long |
| 169 | A9 | No label or date string specified |
| 170 | AA | No or incorrect printer card found |
| 171 | AB | Printer not on |
| 172 | AC | Number of arguments in USB MEMDUMP and USB PMEMDUMP must be 3 |
| 173 | AD | Wrong disk format, image is single sided/ single density |
| 174 | AE | Wrong disk format, image is single sided/double density |
| 175 | AF | Wrong disk format, image is double sided/single density |
| 176 | B0 | Incorrect EF flag specified |
| 177 | B1 | 80 column card not found |
| 178 | B2 | RAM bank file not found |
| 179 | B3 | USB transfer timeout |
| 180 | B4 | USB transfer error |
| 181 | B5 | Two file names required |
| 182 | B6 | Card type not found |
| 183 | B7 | Network error |
| 184 | B8 | Online features disabled |
| 185 | B9 | Server error |
| 186 | BA | URL not found |
| 187 | BB | Number of arguments in USB PLOT must be 3 or 4 |
| 188 | BC | Number of arguments in USB LINE or USB ELLIPSE must be 5 |
| 189 | BD | Number of arguments in USB CIRCLE must be 4 |
| 190 | BE | Number of arguments in USB CPEEK must be 1 or 2 |
| 191 | BF | No REM statement found |
| 192 | C0 | Number of arguments in USB CPOKE must be 2 or 3 |

# APPENDIX E – BASIC COMMAND TABLE

This chapter lists all COMX commands and their command code, jump table entry and start address in ROM.

| Command | Command code | Jump table entry | Start Address |
| --- | --- | --- | --- |
|  |  |  | Original COMX | Expansion / DOS | Super Board |
| REM | 80 | 1500 | 31F9 |  |  |
| CLS | 81 | 1502 | 321E |  |  |
| NEW | 82 | 1504 | 1A47 |  |  |
| RUN | 83 | 1506 | 1F76 |  | E36D |
| END | 84 | 1508 | 10CC |  |  |
| LET | 85 | 150A | 2500 |  |  |
| PRINT | 86 | 150C | 2800 |  |  |
| PR | 86 |  |  |  |  |
| GOTO | 87 | 150E | 312A |  |  |
| IF | 88 | 1510 | 2600 |  |  |
| INPUT | 89 | 1512 | 26C8 |  |  |
| LIST | 8A | 1514 | 1570 |  |  |
| GOSUB | 8B | 1516 | 2F3C |  |  |
| RETURN | 8C | 1518 | 2F30 |  |  |
| WAIT | 8D | 151A | 31D2 |  |  |
| DIM | 8E | 151C | 2100 |  |  |
| FOR | 8F | 151E | 2300 |  |  |
| NEXT | 90 | 1520 | 2F00 |  |  |
| FIXED | 91 | 1522 | 2EE/ |  |  |
| POKE | 92 | 1524 | 2ABD |  |  |
| DEG | 93 | 1526 | 33FA |  |  |
| RAD | 94 | 1528 | 33FD |  |  |
| MUSIC | 95 | 152A | 41CC |  |  |
| DEFINT | 96 | 152C | 38E4 |  |  |
| PSAVE | 97 | 152E | 1672 |  |  |
| PLOAD | 98 | 1530 | 0E00 |  | FCD6 |
| DEFUS | 99 | 1532 | 3EFE |  |  |
| EOP | 9A | 1534 | 25DA |  |  |
| DATA | 9B | 1536 | 3234 |  |  |
| READ | 9C | 1538 | 3D00 |  |  |
| RESTORE | 9D | 153A | 25F4 |  |  |
| EOD | 9E | 153C | 25DD |  |  |
| CLD | 9F | 153E | 2BE9 |  |  |
| DSAVE | A0 | 1540 | 1675 |  |  |
| DLOAD | A1 | 1542 | 0E03 |  | FCDC |
| TIMEOUT | A2 | 1544 | 0EE9 |  |  |
| NOISE | A3 | 1546 | 41D4 |  |  |
| SCREEN | A4 | 1548 | 0BC8 |  |  |
| COLOR | A5 | 154A | 0BFC |  |  |
| CTONE | A6 | 154C | 0D63 |  |  |
| TRACE | A7 | 154E | 2E00 |  |  |
| CALL | A8 | 1550 | 2C00 |  | E373 |
| VOLUME | A9 | 1552 | 0D37 |  | 0D36 |
| TONE | AA | 1554 | 41D0 |  |  |
| SHAPE | AB | 1556 | 0A85 |  |  |
| DOS | AC | 1558 | 0DD9 | E817 | E010 |
| POUT | AD | 155A | 0DD4 | Not available | Not available |
| CARD |  |  | Not available | E817 | E817 |
| EXIT | AE | 155C | 32D0 |  |  |
| TIME | AF | 155E | 1600 |  |  |
| CPOS | B0 | 1560 | 0F00 |  |  |
| RENUMBER | B1 | 1562 | 221C |  | E714 |
| EDIT | B2 | 1564 | 1808 |  | E678 |
| FORMAT | B3 |  | 2D3F |  |  |
| TOUT | B4 | 1568 | 14D4 | 14D4 | Not available |
| USB |  |  | Not available | Not available | F816 |
| AND | B5 |  |  |  |  |
| XOR | B6 |  |  |  |  |
| OR | B7 |  |  |  |  |
| CHR$ | B9 |  |  |  |  |
| MID$ | BA |  |  |  |  |
| ^ | BB |  |  |  |  |
| TAB | BC |  |  |  |  |
| >= | BD |  |  |  |  |
| <= | BE |  |  |  |  |
| <> | BF |  |  |  |  |
| STEP | C0 |  |  |  |  |
| TO | C1 |  |  |  |  |
| , | C2 |  |  |  |  |
| ; | C3 |  |  |  |  |
| ) | C4 |  |  |  |  |
| THEN | C5 |  |  |  |  |
| < | C6 |  |  |  |  |
| > | C7 |  |  |  |  |
| + | C8 |  |  |  |  |
| - | C9 |  |  |  |  |
| * | CA |  |  |  |  |
| / | CB |  |  |  |  |
| = | CC |  |  |  |  |
| : | CD |  |  |  |  |
| " (close) | CE |  |  |  |  |
| " (open) | CF | 159E | 00FE |  |  |
| CHAR | D1 | 15A2 | 2C6A |  |  |
| INT | D2 | 15A4 | 2BB8 |  |  |
| SIN | D4 | 15A8 | 2999 |  |  |
| COS | D5 | 15AA | 299C |  |  |
| ( | D6 |  |  |  |  |
| string var | D7 | 15AE | 2400 |  |  |
| ATN | D8 | 15B0 | 299F |  |  |
| EXP | D9 | 15B2 | 29A2 |  |  |
| LOG | DA | 15B4 | 29A5 |  |  |
| SQR | DB | 15B6 | 29A8 |  |  |
| INT | DC | 15B8 | 1F00 |  |  |
| PEEK | DD | 15BA | 30E8 |  |  |
| ABS | DE | 15BC | 3FA5 |  |  |
| RND | DF | 15BE | 2900 |  |  |
| USR | E0 | 15C0 | 2C03 |  | E379 |
| INUM | E1 | 15C2 | 2B03 |  |  |
| # |  | 15C4 | 2D00 |  |  |
| FNUM | E3 | 15C6 | 27C1 |  |  |
| ASC | E4 | 15C8 | 28B2 |  |  |
| LEN | E5 | 15CA | 306D |  |  |
| \ | E6 |  |  |  |  |
| SGN | E7 | 15CE | 2A74 |  |  |
| MOD | E8 | 15D0 | 1A80 |  |  |
| NOT | EA | 15D4 | 19ED |  |  |
| PI | EB | 15D6 | 24E2 |  |  |
| FVAL | EC | 15D8 | 28AF |  |  |
| STR$ | ED |  |  |  |  |
| MEM | EE | 15DC | 3037 |  |  |
| KEY | F0 | 15E0 | 163F |  |  |